## Slide 1: 第8章
嵌入式系统和Cortex-M3
Notes: Chapter 8
Embedded System and Cortex-M3

## Slide 2
8.1 嵌入式系统
8.1.1 定义
嵌入式系统是用来实现一种或多种功能并且常常带有实时计算要求的计算机系统, 它作为一个完整设备的嵌入部分。
一般用途的计算机, 比如个人电脑 (PC), 常常设计得很灵活并且能满足最终用户的广泛需求。
Notes: 8.1 Embedded System
8.1.1 Definition
An embedded system is a computer system designed to perform one or a few dedicated functions often with real-time computing constraints.
It is embedded as part of a complete device.
A general-purpose computer, such as a personal computer (PC), is designed to be flexible and to meet a wide range of end-user needs.

## Slide 3
8.1.2 历史
20世纪30年代到40年代, 计算机常常只致力于完成一个任务, 它太大又太贵。
阿波罗导航电脑属于第一批现代嵌入式系统,由麻省理工的Charles Stark Draper发明。
Intel 4004是第一个微处理器。
20世纪80年代中期, 大部分外部系统组件已经被集成到了同一芯片上。微控制器的集成增加了传统计算机不会有的应用。
Notes: 8.1.2 History
In the 1930–40s, computers were sometimes dedicated to a single task, but were far too large and expensive.
One of the first recognizably modern embedded systems was the Apollo Guidance Computer, developed by Charles Stark Draper at the MIT.
The first microprocessor, the Intel 4004, was designed for calculators and other small systems.
By the mid-1980s, most of the common previously external system components had been integrated into the same chip.
The integration of microcontrollers has increased the applications for which traditionally a computer would not.

## Slide 4
8.1.3 特征
1. 嵌入式系统用来完成一些特殊的任务。
一些嵌入式系统有实时性要求; 另一些嵌入式系统在实时性能方面的要求会低些或者没有要求。
2. 许多嵌入式系统由在一个大设备里提供通用功能的小电脑零件组成。
3. 为嵌入式系统所写的程序指令被称为固件，被存储在只读存储器或者Flash存储器芯片内。
Notes: 8.1.3 Characteristics
1. Embedded systems are designed to do some specific task.
Some also have real-time performance constraints that must be met; others may have low or no performance requirements.
2. Many embedded systems consist of small, computerized parts within a larger device that serves a more general purpose.
3. The program instructions written for embedded systems are referred to as firmware, and are stored in read-only memory or Flash memory chips.

## Slide 5
8.1.4 应用
嵌入式系统渗透现代生活的各个方面，如:
电信系统。从移动电话到电话交换机，应用了很多嵌入式系统。
消费类电子产品。如：PDAs, mp3等。
交通系统。从飞机到汽车越来越多地使用嵌入式系统。
Notes: 8.1.4 Application
Embedded systems span all aspects of modern life and there are many examples of their use.
Telecommunications systems employ numerous embedded systems from telephone switches for the network to mobile phones at the end-user.
Consumer electronics include
personal digital assistants (PDAs),
mp3 players, mobile phones
and videogame consoles.

## Slide 6
8.1.5 嵌入式系统中的处理器
嵌入式处理器可以分为两大类:
  微处理器 (μP)
  微控制器 (μC)
Notes: 8.1.5 Processors in Embedded Systems
Embedded processors can be broken into two broad categories: ordinary microprocessors (μP) and microcontrollers (μC).
1. A fairly large number of basic CPU architectures are used.
Von Neumann as well as Harvard architectures.
RISC as well as non-RISC and VLIW.
2. Word lengths vary from 4-bit to 64-bits and beyond (mainly in DSP processors).
3. Most architectures come in a large number of different variants and shapes.

## Slide 7
ARM
ARM Advanced RISC Machine公司,
Acorn RISC Machine公司（先前的名称）
截至2007年, 每年销量达十几亿的手机中大约98%使用了至少一个ARM处理器。
截至2009年，ARM处理器大约占所有嵌入式32位RISC处理器的90%。
Notes: ARM
ARM, a company was known as the Advanced RISC
Machine, and before that as the Acorn RISC Machine.
As of 2007, about 98 percent of the more than one billion mobile phones sold each year use at least one ARM processor.
As of 2009, ARM processors account for approximately 90% of all embedded 32-bit RISC processors.
ARM processors are used extensively in consumer electronics, including PDAs, mobile phones, digital media and music players.

## Slide 8
8.2 Cortex-M3概述
Notes: 8.2 Overview of Cortex-M3
A Simplified View of the Cortex-M3

## Slide 9
32-bit微处理器： 32-bit 数据路径, 32-bit 寄存器组, 32-bit 存储器接口。
哈佛架构: 独立的指令总线和数据总线。允许指令和数据在同一时间产生。
存储空间: 4GB。
寄存器: 寄存器 (R0 到 R15) 和 特殊寄存器。
运行模式: 线程模式和handler模式;特权级和用户级。
中断和异常: 内置在嵌套向量中断控制器; 支持11 种系统异常外加240 种外部 IRQ。
Notes: 1. 32-bit microprocessor: 32-bit data path, 32-bit register bank, 32-bit memory interfaces.
2. Harvard architecture: A separate instruction bus and data bus. This allows instructions and data accesses to take place at the same time.
3. Memory space: 8GB.
4. Registers: Registers (R0 to R15) and special registers.
5. Operation Modes: Thread mode and handler mode; Privileged level and user level.
6. Interrupts and Exceptions: The built-in Nested Vectored Interrupt Controller; Support 11 system exceptions plus 240 external IRQs.

## Slide 10
总线接口: 若干总线接口允许 Cortex-M3 同时取指令和取数据。
MPU: 一个可选的存储器保护单元，允许对特权访问和用户程序访问制定访问规则。
指令集: Thumb-2 指令集; 允许 32-位指令和16-位指令被同时使用。
固定的内部调试组件: 提供调试操作支持和像断点调试这样的功能。
Notes: 7. The Bus Interface: Several bus interfaces allow the Cortex-M3 to carry instruction fetches and data accesses at the same time.
8. MPU: An optional Memory Protection Unit allows access rules to be set up for privileged access and user program access.
9. The Instruction Set: Thumb-2 instruction set; allows 32-bit instructions and 16-bit instructions to be used together.
10. Fixed internal debugging components: Provide debugging operation supports and features such as breakpoints.

## Slide 11
8.3 Cortex-M3 基础
8.3.1 寄存器
8.3.1.1 通用寄存器
1. R0~R7 (低寄存器):
可以被所有 16-bit Thumb 指令和所有 32-bit Thumb-2 指令访问。
2. R8~R12 (高寄存器):
可以被所有 Thumb-2 指令但不能被所有 16-bit Thumb 指令访问。
Notes: 8.3 Cortex-M3 Basics
8.3.1 Registers
8.3.1.1 General-Purpose Registers
1. R0~R7 (low registers):
Accessed by all 16-bit Thumb instructions and all 32-bit Thumb-2 instructions.
2. R8~R12 (high registers):
Accessible by all Thumb-2 instructions but not by all 16-bit Thumb instructions.

## Slide 12
Notes: Registers in the Cortex-M3

## Slide 13
8.3.1.2 堆栈指针
R13 ：两个堆栈指针，它们是banked，同一时刻只能使用其中的一个。
堆栈指针的最低两位总是0, 这意味着他们总是字对齐。
两个堆栈指针是:
1. 主堆栈指针(MSP) : 这是默认的堆栈指针。
2. 进程堆栈指针(PSP) : 被基本级别的应用程序代码所使用。
Notes: 8.3.1.2 Stack Pointers
R13 is the stack pointer. Two stack pointers are banked so that only one is visible at a time.
The lowest two bits of the stack pointers are always 0, which means they are always word aligned.
The two stack pointers are:
1. Main Stack Pointer (MSP) : This is the default stack pointer
2. Process Stack Pointer (PSP) : Used by the base-level application code.

## Slide 14
堆栈指针用来进行堆栈存储器操作，比如PUSH和POP。
堆栈存储器的基本概念
Notes: The stack pointers are used for accessing stack memory processes such as PUSH and POP.
Basic Concept of Stack Memory

## Slide 15
汇编语言的语法:
PUSH {R0} ; R13←R13-4, then Memory[R13]←R0
POP {R0} ; R0←Memory[R13], then R13←R13+4
你可以在一条指令中PUSH或POP多个寄存器:
subroutine_1
PUSH {R0-R7, R12, R14} ; Save registers
… ; Do your processing
POP {R0-R7, R12, R14} ; Restore registers
BX R14 ; Return to calling function
Notes: The assembly language syntax is:
PUSH {R0} ; R13R13-4, then Memory[R13] R0
POP {R0} ; R0 Memory[R13], then R13 R13+4
You can PUSH or POP multiple registers in one instruction:
subroutine_1
PUSH {R0-R7, R12, R14} ; Save registers
… ; Do your processing
POP {R0-R7, R12, R14} ; Restore registers
BX R14 ; Return to calling function

## Slide 16
8.3.1.3 链接寄存器
R14 是链接寄存器 (LR). 当一个子程序或函数被调用时，LR用来存储返回的程序计数器。
当你使用 BL (branch and link) 指令时:
main ; Main program
…
BL function1 ; Call function1 using Branch with Link
; instruction.
; PC = function1 and
; LR = the next instruction in main
…
function1
… ; Program code for function 1
BX LR ; Return
Notes: 8.3.1.3 Link Register
R14 is the link register (LR). LR is used to store the return program counter when a subroutine or function is called.
when you’re using the BL (branch and link) instruction:
main ; Main program
…
BL function1 ; Call function1 using Branch with Link
; instruction.
; PC = function1 and
; LR = the next instruction in main
…
function1
… ; Program code for function 1
BX LR ; Return

## Slide 17
8.3.1.4 程序计数器
R15 是程序计数器。
你可以在汇编语言中通过R15或PC访问它。
当你读这个寄存器时，你会发现它的值和执行指令位置的值相差4。
Example:
0x1000 : MOV R0, PC ; R0 = 0x1004
Notes: 8.3.1.4 Program Counter
R15 is the program counter.
You can access it in assembler code by either R15 or PC.
When you read this register you will find that the value is different than the location of the executing instruction by 4.
Example:
0x1000 : MOV R0, PC ; R0 = 0x1004

## Slide 18
8.3.2 特殊寄存器
Cortex-M3 处理器中的特殊寄存器包括:
1. 程序状态寄存器 (PSRs)
2. 中断屏蔽寄存器(PRIMASK, FAULTMASK, and BASEPRI)
3. 控制寄存器 (CONTROL)
Cortex-M3中的特殊寄存器
Notes: 8.3.2 Special Registers
The special registers in the Cortex-M3 processor include:
1. Program Status Registers (PSRs)
2. Interrupt Mask Registers (PRIMASK, FAULTMASK, and BASEPRI)
3. Control Register (CONTROL)
Special Registers in the Cortex-M3

## Slide 19
8.3.2.1 程序状态寄存器 (PSRs)
程序状态寄存器可以分为三个状态寄存器：
1. 应用 PSR (APSR)
2. 中断 PSR (IPSR)
3. 执行 PSR (EPSR)
 | 31 | 30 | 29 | 28 | 27 | 26:25 | 24 | 23:20 | 19:16 | 15:10 | 9 | 8 | 7 | 6 | 5 | 4:0
xPSR | N | Z | C | V | Q | ICI/IT | T |  |  | ICI/IT |  | Exception Number |  |  |  | 
Cortex-M3中的组合程序状态寄存器
Notes: 8.3.2.1 Program Status Registers (PSRs)
The program status registers are subdivided into three status registers:
1. Application PSR (APSR)
2. Interrupt PSR (IPSR)
3. Execution PSR (EPSR)
Combined Program Status Registers (xPSR) in the Cortex-M3

## Slide 20
Cortex-M3中的程序状态寄存器 (PSRs)
 | 31 | 30 | 29 | 28 | 27 | 26:25 | 24 | 23:20 | 19:16 | 15:10 | 9 | 8 | 7 | 6 | 5 | 4:0
APSR | N | Z | C | V | Q |  |  |  |  |  |  |  |  |  |  | 
IPSR |  |  |  |  |  |  |  |  |  |  |  | Exception Number |  |  |  | 
EPSR |  |  |  |  |  | ICI/IT | T |  |  | ICI/IT |  |  |  |  |  | 
EPSR 和IPSR 是只读的:
MRS r0, APSR ; Read Flag state into R0
MRS r0, IPSR ; Read Exception/Interrupt state
MRS r0, EPSR ; Read Execution state
MSR APSR, r0 ; Write Flag state
Notes: Program Status Registers (PSRs) in the Cortex-M3
EPSR and IPSR are read-only:
MRS r0, APSR ; Read Flag state into R0
MRS r0, IPSR ; Read Exception/Interrupt state
MRS r0, EPSR ; Read Execution state
MSR APSR, r0 ; Write Flag state

## Slide 21
Bit | Description
N | 负
Z | 零
C | 进位/借位
V | 溢出
Q | 置顶饱和标记
ICI/IT | 中断可持续指令(ICI) 位, IF-THEN 指令状态位
T | Thumb 状态, 总是 1; 试图清除此位将导致错误异常
异常号 | 指出处理器正在处理哪一个异常
Cortex-M3 中程序状态寄存器的位域
Notes: Bit Fields in Cortex-M3 Program Status Registers
Bit Description
N Negative
Z Zero
C Carry/borrow
V Overflow
Q Sticky saturation flag
ICI/IT Interrupt-Continuable Instruction (ICI) bits, IF-THEN instruction status bit
T Thumb state, always 1; trying to clear this bit will cause a fault exception
Exception Number Indicates which exception the processor is handling

## Slide 22
8.3.2.2 PRIMASK, FAULTMASK 和 BASEPRI 寄存器
Cortex-M3 中断屏蔽寄存器
寄存器名 | 描述
PRIMASK | 一个1-bit 寄存器。当置位时, 它允许NMI 和硬fault; 所有其他的中断和异常将被屏蔽。
FAULTMASK | 一个1-bit 寄存器。当置位时, 它只允许NMI, 所有中断和默认异常处理被忽略。
BASEPRI | 一个9位寄存器。它定义了屏蔽优先级。 当它被设成某个值时, 所有同级的或低级的中断被忽略。
Notes: 8.3.2.2 PRIMASK, FAULTMASK and BASEPRI Registers
The PRIMASK, FAULTMASK, and BASEPRI registers are used to disable exceptions.
Cortex-M3 Interrupt Mask Registers
Register Name Description
PRIMASK A 1-bit register. When this is set, it allows NMI and the hard fault exception; all other interrupts and exceptions are masked.
FAULTMASK A 1-bit register. When this is set, it allows only the NMI, and all interrupts and fault handling exceptions are disabled.
BASEPRI A register of up to 9 bits. It defines the masking priority level. When this is set, it disables all interrupts of the same or lower level.

## Slide 23
Example:
MRS r0, BASEPRI ; Read BASEPRI register into R0
MRS r0, PRIMASK ; Read PRIMASK register into R0
MRS r0, FAULTMASK ; Read FAULTMASK register into R0
MSR BASEPRI, r0 ; Write R0 into BASEPRI register
MSR PRIMASK, r0 ; Write R0 into PRIMASK register
MSR FAULTMASK, r0 ; Write R0 into FAULTMASK register
在用户访问级，PRIMASK, FAULTMASK, 和 BASEPRI 寄存器不能被置位。
Notes: To access the PRIMASK, FAULTMASK, and BASEPRI registers, the MRS and MSR instructions are used.
Example:
MRS r0, BASEPRI ; Read BASEPRI register into R0
MRS r0, PRIMASK ; Read PRIMASK register into R0
MRS r0, FAULTMASK ; Read FAULTMASK register into R0
MSR BASEPRI, r0 ; Write R0 into BASEPRI register
MSR PRIMASK, r0 ; Write R0 into PRIMASK register
MSR FAULTMASK, r0 ; Write R0 into FAULTMASK register
The PRIMASK, FAULTMASK, and BASEPRI registers cannot be set in the user access level.

## Slide 24
8.3.2.3 控制寄存器
控制寄存器定义特权级和堆栈指针的选择。这个寄存器有两位。
Cortex-M3 控制寄存器
Bit | Function
CONTROL[1] | 堆栈状态:(当访问级别改变时自动改变) 1 = 进程堆栈(PSP) 被使用 (针对用户级) 0 = 默认堆栈 (MSP) 被使用(针对特权级)
CONTROL[0] | 指定的访问级别: 0 = 特权的线程模式 1 = 用户状态的线程模式
Notes: 8.3.2.3 The Control Register
The Control register is used to define the privilege level and the stack pointer selection. This register has two bits.
Cortex-M3 CONTROL Register
Bit Function
CONTROL[1] Stack status:(automatically changes when access level changes)
1 = Process stack(PSP) is used (for user level)
0 = Default stack (MSP) is used(for privileged level)
CONTROL[0] Specify access level:
0 = Privileged in Thread mode
1 = User state in Thread mode

## Slide 25
CONTROL[1]
在Cortex-M3中, 在handler模式中CONTROL[1] 位总是0 (MSP)。但是, 在线程或基本级别，它可以为0或1。
CONTROL[0]
CONTRL[0] 位只在特权状态可写。
使用MRS和MSR指令来访问控制寄存器:
MRS r0, CONTROL ; Read CONTROL register into R0
MSR CONTROL, r0 ; Write R0 into CONTROL register
Notes: CONTROL[1]
In Cortex-M3, the CONTROL[1] bit is always 0 (MSP)in handler mode. However, in the Thread or base level, it can be either 0 or 1.
CONTROL[0]
The CONTRL[0] bit is writable only in a privileged state.
To access the Control register, the MRS and MSR instructions are used:
MRS r0, CONTROL ; Read CONTROL register into R0
MSR CONTROL, r0 ; Write R0 into CONTROL register

## Slide 26
8.3.3 操作模式
两种模式和两种权限级别。
 | 特权 | 用户
当运行一个异常 | 处理器模式 | 
当运行主程序 | 线程模式 | 线程模式
在Cortex-M3中的操作模式和权限级别
Notes: 8.3.3 Operation Mode
Two modes and two privilege levels.
Operation Modes and Privilege Levels in Cortex-M3
Privileged User
When running an exceptton Handler Mode
When running main program Thread Mode Thread Mode

## Slide 27
特权级别提供了一种机制来保障访问存储器的关键区域，同时还提供了一个基本的安全模式。
通过写Control register[0]=1，软件在特权访问级别可以使程序转换到用户访问级别。
用户程序不能够通过写控制寄存器直接变回特权状态。
它要经过一个异常处理程序设置Control register[0]=0使得处理器切换回特权访问级别。
Notes: The privilege levels provide a mechanism for safeguarding memory accesses to critical regions as well as providing a basic security model.
Software in a privileged access level can switch the program into the user access level by writing the Control register[0]=1.
A user program cannot change back to the privileged state directly by writing to the Control register.
It has to go through an exception handler that programs the Control register [0]=0 to switch the processor back into privileged access level.

## Slide 28
通过控制寄存器或异常来切换操作模式
Notes: Switching of Operation Mode by Programming the Control Register or by Exceptions

## Slide 29
由控制寄存器来定义处理器的模式和访问级别。 当Control register[0] =0, 异常发生时只有处理器的模式发生了变化。 访问级别始终停留在特权状态。
在中断时改变处理器模式
Notes: The mode and access level of the processor are defined by the Control register. When the Control register[0] =0, only the processor mode changes when an exception takes place. Access level stays privileged all the time.
Switching Processor Mode at Interrupt

## Slide 30
对于用户级别程序转换到特权状态, 需要在处理程序产生一个中断 (例如, SVC, 或呼叫系统服务) 和写CONTROL[0]=0。
在中断时切换处理器模式和权限级别
Notes: For a user-level program to switch to privileged state, it has to raise an interrupt (for example, SVC, or System Service Call) and write to CONTROL[0]=0 within the handler.
Switching Processor Mode and Privilege Level at Interrupt

## Slide 31
8.3.4 向量表
向量表是字数据的一个队列。 当使用 PUSH/POP 指令时, 堆栈指针自动地增加/ 减少。
例如:
复位是异常类型1。
复位向量的地址是1乘4, 等于 0x00000004
NMI 向量 (类型 2) 位于2 * 4 = 0x00000008
地址 0x00000000 被用作MSP的开始值。
Notes: 8.3.4 Vector Tables
The vector table is an array of word data.
When PUSH/POP instructions are used, the stack pointer is incremented/ decremented automatically.
Example:
The reset is exception type 1.
The address of the reset vector is 1 times 4, which equals 0x00000004, and NMI vector (type 2) is located in
2 * 4 = 0x00000008
The address 0x00000000 is used as the starting value for the MSP.

## Slide 32
复位后的向量表定义
异常类型 | 偏移地址 | 异常向量
15 | 0x3C | SYSTICK
14 | 0x38 | PendSV
13 | 0x34 | 保留
12 | 0x30 | 调试监视
11 | 0x2C | SVC
7-10 | 0x1C-0x28 | 保留
6 | 0x18 | 使用故障
5 | 0x14 | 总线故障
4 | 0x10 | 存储器管理故障
3 | 0x0C | 硬件故障
2 | 0x08 | NMI
1 | 0x04 | 复位
0 | 0x00 | MSP的开始值
Notes: Vector Table Definition After Reset
Exception Type Address Offset Exception Vector
15 0x3C SYSTICK
14 0x38 PendSV
13 0x34 Reserved
12 0x30 Debug Monitor
11 0x2C SVC
7-10 0x1C-0x28 Reserved
6 0x18 Usage fault
5 0x14 Bus fault
4 0x10 MemManage fault
3 0x0C Hard fault
2 0x08 NMI
1 0x04 Reset
0 0x00 Starting value of the MSP

## Slide 33
8.3.5 栈内存操作
8.3.5.1 栈的基本操作
在寄存器中的数据可以通过PUSH操作保存到栈内存并且通过POP操作在稍后恢复到寄存器.
主程序
...
; R0 = X, R1 = Y, R2 = Z
BL function1
function1
PUSH {R0} ; store R0 to stack & adjust SP
PUSH {R1} ; store R1 to stack & adjust SP
PUSH {R2} ; store R2 to stack & adjust SP
Notes: 8.3.5 Stack Memory Operations
8.3.5.1 Basic Operations of the Stack
Data in registers are saved into stack memory by a PUSH operation and can be restored to registers later by a POP operation.

## Slide 34
... ; Executing task (R0, R1 and R2
; could be changed)
POP {R2} ; restore R2 and SP re-adjusted
POP {R1} ; restore R1 and SP re-adjusted
POP {R0} ; restore R0 and SP re-adjusted
BX LR ; Return
; Back to main program
; R0 = X, R1 = Y, R2 = Z
... ; next instructions

## Slide 35
8.3.5.2 Cortex-M3 的堆栈实现
堆栈指针 (SP) 指向压入堆栈的最后一个数据, SP 在一个新的PUSH操作前递减。
Cortex-M3 堆栈PUSH 实现
Notes: 8.3.5.3 Cortex-M3 Stack Implementation
The stack pointer (SP) points to the last data pushed to the stack memory, and the SP decrements before a new PUSH operation.
Cortex-M3 Stack PUSH Implementation

## Slide 36
对于 POP 操作, 数据从SP指向的存储区域读取, 然后堆栈指针递增。 在存储位置的内容并未发生变化。
Cortex-M3 的堆栈POP 操作实现
Notes: For POP operations, the data is read from the memory location pointer by SP, then the stack pointer is incremented. The contents in the memory location are unchanged.
Cortex-M3 Stack POP Implementation

## Slide 37
8.3.5.3 在Cortex-M3中的两种堆栈模式
Cortex-M3 有两个堆栈指针: 主堆栈指针 (MSP) 和进程堆栈指针(PSP)。被使用的SP 寄存器由控制寄存器的比特1来控制。
Control [1] = 0: 线程模式和handler模式使用主堆栈
Notes: 8.3.5.4 The Two-Stack Model in the Cortex-M3
The Cortex-M3 has two stack pointers: the Main Stack Pointer (MSP) and the Process Stack Pointer (PSP).
The SP register to be used is controlled by the Control register bit 1.
Control [1] = 0: Both Thread Level and Handler Use Main Stack

## Slide 38
Control[1] = 1线程模式使用进程堆栈和handler模式使用主堆栈
Notes: Control[1] = 1: Thread Level Uses Process Stack and Handler Uses Main Stack
The automatic stacking and unstacking mechanism will use PSP; whereas stack operations inside the handler will use MSP.

## Slide 39
8.3.5.4 复位序列
处理器退出复位后，它会从存储器中读取两个字:
1. 从地址 0x00000000处取出MSP的初始值
2. 从地址 0x00000004处取出复位向量(启动程序的起始地址; LSB应该被设为1来说明 Thumb 状态)
Notes: 8.3.5.5 Reset Sequence
After the processor exits reset, it will read two words from memory:
1. Address 0x00000000: holds Starting value of R13 (the stack pointer)
2. Address 0x00000004: holds Reset vector (the starting address of startup program; LSB should be set to 1 to indicate Thumb state)

## Slide 40
复位序列
Notes: Reset Sequence
The vector table starts after the initial SP value. In the Cortex-M3, vector addresses in the vector table should have their LSB set to 1 to indicate that they are Thumb code.

## Slide 41
初始化堆栈指针值和初始化程序计数器 (PC) 值的例子
Notes: Initial Stack Pointer Value and Initial Program Counter (PC) Value Example

## Slide 42
8.4 存储系统
8.4.1 存储系统功能概述
1. 预定义的内存映射指定了在访问内存时使用哪个总线接口。
2. Bit-band: 提供了对内存或外设中位数据的原子操作。
3. 提供了非对齐访问和互斥访问。
Notes: 8.4 Memory System
8.4.1 Memory System Features Overview
1. A predefined memory map that specifies which bus interface is to be used when a memory location is accessed.
2. Bit-band: This provides atomic operations to bit data in memory or peripherals.
3. Supports unaligned transfers and exclusive accesses.

## Slide 43
8.4.2 内存映射
Cortex-M3 处理器有一个固定的存储映射。一些存储单元分配给了私有外设，如：
1. 取补丁和断点单元 (FPB)
2. 数据观察点和跟踪单元(DWT)
3. 仪表跟踪宏单元(ITM)
4. 嵌入式跟踪宏单元(ETM)
5. 跟踪端口接口单元(TPIU)
6. ROM 表
Cortex-M3 处理器总共有 4 GB 的地址空间。
Notes: 8.4.2 Memory Maps
The Cortex-M3 processor has a fixed memory map.
Some of the memory locations are allocated for private peripherals such as debugging components.
1. Fetch Patch and BreakPoint Unit (FPB)
2. Data WatchPoint and Trace Unit (DWT)
3. Instrumentation Trace Macrocell (ITM)
4. Embedded Trace Macrocell (ETM)
5. Trace Port Interface Unit (TPIU)
6. ROM Table
The Cortex-M3 processor has a total of 4 GB of address space.

## Slide 44
Notes: A Cortex-M3 Predefined Memory Map

## Slide 45
片上SRAM: 0.5 GB。 SRAM存储范围是用来连接内部的SRAM。
片上外设: 0.5 GB，支持 bit-band 别名并且可以通过系统总线接口访问。
片外RAM: 1 GB。允许执行程序。
外部设备: 1 GB。不允许执行程序。
系统级组件+ 内部专用的外围总线+ 外部私有外设总线+ 供应商特定系统外设 0.5 GB.
Notes: SRAM:
0.5 GB. The SRAM memory range is for connecting internal SRAM.
On-chip peripherals:
0.5 GB, supports bit-band alias and is accessed via the system bus interface.
External RAM:
1 GB. Program execution is allowed.
External devices:
1 GB. Program execution is not allowed.
System-level components + internal private peripheral buses + external private peripheral bus + vendor-specific system peripherals:
0.5 GB.

## Slide 46
私有外设总线:
1. AHB 私有外设总线, 只针对 Cortex-M3 内部 AHB 外设。
2. APB 私有外设总线, 针对 Cortex-M3 内部 APB 设备和外围设备。
Notes: Private peripheral bus:
1. AHB private peripheral bus, for Cortex-M3 internal AHB peripherals only.
2. APB private peripheral bus, for Cortex-M3 internal APB devices as well as external peripherals.

## Slide 47
8.4.3 内存访问属性
存储器映射定义了内存的访问属性（4种）:
Bufferable
Cacheable
Executable
Sharable
Notes: 8.4.3 Memory Access Attributes
The memory map defines the memory attributes of the access:
The default memory attribute settings can be overridden if MPU is present and the region is programmed differently from the default.

## Slide 48
区域 | 地址 | 用于 | 可缓存 | 可执行, 缓冲
代码存储区 | 0x00000000–0x1FFFFFFF |  | WT (只写) | 可执行, 缓冲
SRAM 存储区域 | 0x20000000–0x3FFFFFFF | 片上RAM | WB-WA (写回, 写分配) | 可执行, 缓冲
周边地区 | 0x40000000–0x5FFFFFFF | 外设 | 非缓存 | 非缓存
外部 RAM 区域 | 0x60000000–0x7FFFFFFF | 片上或片外存储器 | WB-WA (写回, 写分配) | 可执行
外部 RAM 区域 | 0x80000000–0x9FFFFFFF | 片上或片外存储器 | WT (直写) | 可执行
外部设备 | 0xA0000000–0xBFFFFFFF | 外部设备和/或共享内存 |  | 不可执行, 非缓冲
外部设备 | 0xC0000000–0xDFFFFFFF | 外部设备和/或共享内存 |  | 不可执行, 非缓冲
系统区域 | 0xE0000000–0xFFFFFFFF | 私有外设 | 非缓存 | 不可执行, 非缓冲
系统区域 | 0xE0000000–0xFFFFFFFF | 供应商特定设备 | 非缓存 | 不可执行, 非缓冲
空间划分和缺省属性

## Slide 49
8.4.4 Bit-Band操作
Bit-band操作支持使用普通的加载/存储指令来对单一的bit进行读/写操作。
Bit-band区域:
  1. 片上SRAM 的第一个1MB区域
  2. 片上外设的第一个1 MB
它们可以通过一个单独的被称为bit-band alias（位带别名区）的存储区域来访问。
Notes: 8.4.5 Bit-Band Operations
Bit-band operation support allows a single load/store operation to access (read/write) to a single data bit.
Bit-band regions:
1. The first 1 MB of the SRAM region
2. The first 1 MB of the peripheral region
They can be accessed via a separate memory region called the bit-band alias.

## Slide 50
通过Bit-Band Alias访问Bit-Band Region
Notes: Bit Accesses to Bit-Band Region Via the Bit-Band Alias

## Slide 51
设置地址0x20000000中的字数据的位2
Notes: To set bit 2 in word data in address 0x20000000:

## Slide 52
汇编序列
写:
1. 不使用Bit-Band:
LDR R0, =0x20000000 ; Setup address
LDR R1, [R0] ; Read
ORR.W R1, #0x4 ; Modify bit
STR R1, [R0] ; Write back result
2. 使用Bit-Band:
LDR R0, =0x22000008 ; Setup address
MOV R1, #1 ; Setup data
STR R1, [R0] ; Write
Notes: The assembler sequence to
Write:
1. Without Bit-Band:
2. With Bit-Band:

## Slide 53
从Bit-Band Alias读
Notes: Read from the Bit-Band Alias

## Slide 54
汇编序列进行读:
1. 使用 Bit-Band:
LDR R0, =0x20000000 ; Setup address
LDR R1, [R0] ; Read
UBFX.W R1, R1, #2, #1 ; Extract bit[2]
2. 使用 Bit-Band:
LDR R0, =0x22000008 ; Setup address
LDR R1, [R0] ; Read
Notes: The assembler sequence to read:
1. With Bit-Band:
LDR R0, =0x20000000 ; Setup address
LDR R1, [R0] ; Read
UBFX.W R1, R1, #2, #1 ; Extract bit[2]
2. With Bit-Band:
LDR R0, =0x22000008 ; Setup address
LDR R1, [R0] ; Read

## Slide 55
位带别名区地址
对于SRAM位带区的某个bit，记它所在字节地址为 A,位序号为n(0<=n<=7)，则该bit在别名区的地址为：
AliasAddr =0x22000000+ (A-0x20000000)*32 + n*4
对于片上外设位带区的某个bit，记它所在字节的地址为 A,位序号为n(0<=n<=7)，则该比特在别名区的地址为：
AliasAddr =0x 42000000+ (A-0x40000000)*32 + n*4

## Slide 56
SRAM 区域的Bit-Band 地址重映射
外设存储区 Bit-Band 地址重映射
Bit-Band 区域 | 别名等效
0x20000000 bit[0] | 0x22000000 bit[0]
0x20000000 bit[1] | 0x22000004 bit[0]
0x20000000 bit[2] | 0x22000008 bit[0]
… | …
0x20000000 bit[31] | 0x2200007C bit[0]
0x20000004 bit[0] | 0x22000080 bit[0]
… | …
0x20000004 bit[31] | 0x220000FC bit[0]
… | …
0x200FFFFC bit[31] | 0x23FFFFFC bit[0]
Bit-Band 区域 | 别名等效
0x40000000 bit[0] | 0x42000000 bit[0]
0x40000000 bit[1] | 0x42000004 bit[0]
0x40000000 bit[2] | 0x42000008 bit[0]
… | …
0x40000000 bit[31] | 0x4200007C bit[0]
0x40000004 bit[0] | 0x42000080 bit[0]
… | …
0x40000004 bit[31] | 0x420000FC bit[0]
… | …
0x400FFFFC bit[31] | 0x43FFFFFC bit[0]

## Slide 57
8.4.5 未对齐数据传递
Cortex-M3 支持在单一的访问中使用未对齐的传递。
1. 字, 地址不是4的倍数
 | Byte 3 | Byte 2 | Byte 1 | Byte 0
Address N+4 |  |  |  | [31:24]
Address N | [23:16] | [15:8] | [7:0] | 
 | Byte 3 | Byte 2 | Byte 1 | Byte 0
Address N+4 |  |  | [31:24] | [23:16]
Address N | [15:8] | [7:0] |  | 
 | Byte 3 | Byte 2 | Byte 1 | Byte 0
Address N+4 |  | [31:24] | [23:16] | [15:8]
Address N | [7:0] |  |  | 
Notes: Example:
1. Set address 0x20000000 to a value of 0x3355AACC.
2. Read address 0x22000008. This read access is remapped into read access to 0x20000000. The return value is 1 (bit[2] of 0x3355AACC).
3. Write 0x0 to 0x22000008.
4. Now read 0x20000000. That gives you a return value of 0x3355AAC8 (bit[2] cleared).
8.4.6 Unaligned Transfers
The Cortex-M3 supports unaligned transfers on single accesses. Data memory accesses can be defined as aligned or unaligned.

## Slide 58
2. 半字, 地址不是2的倍数
 | Byte 3 | Byte 2 | Byte1 | Byte 0
Address N+4 |  |  |  | 
Address N |  | [15:8] | [7:0] | 
 | Byte 3 | Byte 2 | Byte 1 | Byte 0
Address N+4 |  |  |  | [15:8]
Address N | [7:0] |  |  | 
Notes: 2. Half word size, and the address is not a multiple of 2.

## Slide 59
未对齐的数据传送只发生在常规的数据传送指令中，其他指令不支持，如：
  1. 多个数据的载入/存储
  2. 堆栈操作(PUSH/POP)
  3. 互斥访问
  4. bit-band 操作
非对齐传递事实上在内部通过处理器的总线接口单元转换成若干个对齐传递。
Notes: There are a number of limitations:
1. Not supported in Load/Store multiple instructions.
2. Stack operations (PUSH/POP) must be aligned.
3. Exclusive accesses must be aligned。
4. Unaligned transfers are not supported in bit-band operations.
When unaligned transfers are used, they are actually converted into multiple aligned transfers by the processor’s bus interface unit.

## Slide 60
8.4.6 互斥访问（Exclusive Accesses）
互斥体在多任务环境中使用，也在中断服务例程和主程序之间使用，用于给任务申请共享资源（如一块共享内存）。在某个（排他型）共享资源被一个任务拥有后，直到这个任务释放它之前，其它任务不得再访问它。
为建立一个互斥体，需要定义一个标志变量，用来指示其对应的共享资源是否已经被某任务拥有。当另一个任务欲取得此共享资源时，它要先检查这个互斥体，以获知共享资源是否无人使用。
Notes: 8.4.7 Exclusive Accesses
SWP instruction (swap) was used for semaphore operations in traditional ARM processors.
1. What is semaphore?(信号灯)
Semaphores are commonly used for allocating shared resources to applications. It is locked to that process When a resource is being used by one process
2. Why is exclusive access used instead of SWP instruction?
When a process or application want to use the resource, it needs to check whether the resource has been locked first. If it is not being used, it can indicate that the resource is locked.

## Slide 61
独占访问指令包括:
1. LDREX
2. STREX
例子:
TryInc
LDREX r2, [R0]
ADD r2, #1
STREX R1, R2, [R0]
CMP R1, #1 ;检查STREX 是否被驳回
BEQ TryInc ;如果发现STREX 被驳回，则重试。
Notes: Exclusive access instructions include:
1. LDREX (word)
2. LDREXB (byte)
3. LDREXH (half word)
4. STREX (word)
5. STREXB (byte)
6. and STREXH (half word)
Examples of LDREX/STREX:
LDREX <Rxf>, [Rn, #offset]
STREX <Rd>, <Rxf> ,[Rn, #offset]

## Slide 62
8.4.7 端模式
Cortex-M3 支持小端模式和大端模式。
在 Cortex-M3 中大端模式的定义和 ARM7 中不同。
在 ARM7TDMI中, 大端模式被称为字不变大端模式, 然而在 Cortex-M3中, 大端模式被称为字节不变大端模式。
在AHB 总线上的 BE-8 模式下，数据传输使用和小端模式中一样的字节通道。
Notes: 8.4.8 Endian Mode
The Cortex-M3 supports both little endian and big endian modes.
The definition of big endian in the Cortex-M3 is different from the ARM7’s.
In the ARM7TDMI, the big endian scheme is called word-invariant big endian, whereas in the Cortex-M3, the big endian scheme is called byte-invariant big endian.
The data transfer on the AHB bus in BE-8 mode uses the same data byte lanes as in little endian.

## Slide 63
Address, Size | Bits 31-24 | Bits 23-16 | Bits 15-8 | Bits 7-0
0x1000, 字 | Data[7:0] | Data[15:8] | Data[23:16] | Data[31:24]
0x1000, 半字 |  |  | Data[7:0] | Data[15:8]
0x1002, 半字 | Data[7:0] | Data[15:8] |  | 
0x1000, 字节 |  |  |  | Data[7:0]
0x1001, 字节 |  |  | Data[7:0] | 
0x1002, 字节 |  | Data[7:0] |  | 
0x1003, 字节 | Data[7:0] |  |  | 
Cortex-M3 (字节不变大端模式): AHB 总线上的数据
Notes: The Cortex-M3 (Byte-Invariant Big Endian): Data on AHB Bus
Address, Size Bits 31-24 Bits 23-16 Bits 15-8 Bits 7-0
0x1000, word Data[7:0] Data[15:8] Data[23:16] Data[31:24]
0x1000, half word Data[7:0] Data[15:8]
0x1002, half word Data[7:0] Data[15:8]
0x1000, byte Data[7:0]
0x1001, byte Data[7:0]
0x1002, byte Data[7:0]
0x1003, byte Data[7:0]

## Slide 64
ARM7 (字不变大端模式): AHB 总线上的数据
Address, Size | Bits 31-24 | Bits 23-16 | Bits 15-8 | Bits 7-0
0x1000, 字 | Data[7:0] | Data[15:8] | Data[23:16] | Data[31:24]
0x1000, 半字 | Data[7:0] | Data[15:8] |  | 
0x1002, 半字 |  |  | Data[7:0] | Data[15:8]
0x1000, 字节 | Data[7:0] |  |  | 
0x1001, 字节 |  | Data[7:0] |  | 
0x1002, 字节 |  |  | Data[7:0] | 
0x1003, 字节 |  |  |  | Data[7:0]
Notes: The data transfer on the AHB bus in BE-8 mode uses the same data byte lanes as in little endian. The data byte inside the half word or word data is reversely ordered.
ARM7 (Word-Invariant Big Endian): Data on AHB Bus
Address, Size Bits 31-24 Bits 23-16 Bits 15-8 Bits 7-0
0x1000, word Data[7:0] Data[15:8] Data[23:16] Data[31:24]
0x1000, half word Data[7:0] Data[15:8]
0x1002, half word Data[7:0] Data[15:8]
0x1000, byte Data[7:0]
0x1001, byte Data[7:0]
0x1002, byte Data[7:0]
0x1003, byte Data[7:0]

## Slide 65
8.5 指令集
8.5.1 指令列表
16-Bit 数据处理指令
指令 | 功能
ADC | 带进位加
ADD | 加
AND | 逻辑与
BIC | 位清零 (一个值与另一个值的逻辑反转进行逻辑与)
CMN | 负比较(将一个数据和另一个数据的二进制补码进行比较同时更新标志 )
CMP | 比较 (比较两个数据并且更新标志)
CPY | 拷贝 (从架构v6开始可用; 把一个高或低寄存器中的值移植到另一个高或低寄存器)
LSL | 逻辑左移
LSR | 逻辑右移
MOV | 移动 (可用于寄存器至寄存器的传输或加载即时数据)
MUL | 乘
Notes: 8.5.2 Instruction List
16-Bit Data Processing Instructions
Instruction Function
ADC Add with carry
ADD Add
AND Logical AND
BIC Bit clear (Logical AND one value with the logic inversion of another value)
CMN Compare negative (compare one data with two’s complement of another data and update flags)
CMP Compare (compare two data and update flags)
CPY Copy (available from architecture v6; move a value from one high or low register to
another high or low register)
LSL Logical shift left
LSR Logical shift right
MOV Move (can be used for register-to-register transfers or loading immediate data)
MUL Multiply

## Slide 66
MVN | Move NOT (获得逻辑反转值)
NEG | 取反 (获得二进制补码)
ORR | 逻辑或
ROR | 向右旋转
SBC | 减去进位
SUB | 减
TST | 测试(被用作逻辑 与; Z 标志会更新但是与的结果不会被储存 )
REV | 反转在一个32-位寄存器中的字节顺序 (从架构v6开始可用)
SXTB | 带符号延长字节 (从架构v6开始可用)
SXTH | 带符号延长半字 (从架构v6开始可用)
UXTB | 不带符号延长字节(a从架构v6开始可用)
UXTH | 不带符号延长半字 (从架构v6开始可用)
(Continued)
Notes: MVN Move NOT (obtain logical inverted value)
NEG Negate (obtain two’s complement value)
ORR Logical OR
ROR Rotate right
SBC Subtract with carry
SUB Subtract
TST Test (use as logical AND; Z flag is updated but AND result is not stored)
REV Reverse the byte order in a 32-bit register (available from architecture v6)
SXTB Signed extend byte (available from architecture v6)
SXTH Signed extend half word (available from architecture v6)
UXTB Unsigned extend byte (available from architecture v6)
UXTH Unsigned extend half word (available from architecture v6)

## Slide 67
16-Bit 分支指令
指令 | 功能
B | 分支
B<cond> | 条件分支
BL | 带连接的分支; 调用一个子程序，并在LR中存储返回地址
BLX | 带连接的分支和改变状态 (只有BLX <reg>)
CBZ | 进行比较如果为0就跳转(架构 v7)
CBNZ | 进行比较如果非0就跳转(架构 v7)
IT | IF-THEN (架构 v7)
Notes: 16-Bit Branch Instructions
Instruction Function
B Branch
B<cond> Conditional branch
BL Branch with link; call a subroutine and store the return address in LR
BLX Branch with link and change state (BLX <reg> only)
CBZ Compare and branch if zero (architecture v7)
CBNZ Compare and branch if nonzero (architecture v7)
IT IF-THEN (architecture v7)

## Slide 68
16-Bit 加载和存储指令
指令 | 功能
LDR | 从存储器中加载字到寄存器
LDRH | 从存储器中加载半字到寄存器
LDRB | 从存储器中加载字节到寄存器
STR | 从寄存器中存储字到存储器
STRH | 从寄存器中存储半字到存储器
STRB | 从寄存器中存储字节到存储器
LDMIA | 加载多个后增量
STMIA | 存储多个后增量
PUSH | Push 多个寄存器
POP | Pop 多个寄存器
Notes: 16-Bit Load and Store Instructions
Instruction Function
LDR Load word from memory to register
LDRH Load half word from memory to register
LDRB Load byte from memory to register
STR Store word from register to memory
STRH Store half word from register to memory
STRB Store byte from register to memory
LDMIA Load multiple increment after
STMIA Store multiple increment after
PUSH Push multiple registers
POP Pop multiple registers

## Slide 69
另外的 16-Bit 指令
指令 | 功能
SVC | 系统服务呼叫
BKPT | 断点; 如果启用了调试, 会进入调试模式 (停止), 或者如果启用了调试监控异常, 将调用调试异常; 否则会调用一个错误异常
NOP | 无操作
CPSIE | 启用 PRIMASK (CPSIE i)/FAULTMASK (CPSIE f ) 寄存器 (设置寄存器为0)
CPSID | 禁用 PRIMASK (CPSID i)/ FAULTMASK (CPSID f ) 寄存器 (设置寄存器为1)
Notes: Other 16-Bit Instructions
Instruction Function
SVC System service call
BKPT Breakpoint; if debug is enabled, will enter debug mode (halted), or if debug monitor exception is enabled, will invoke the debug exception; otherwise it will invoke
a fault exception
NOP No operation
CPSIE Enable PRIMASK (CPSIE i)/FAULTMASK (CPSIE f ) register (set the register to 0)
CPSID Disable PRIMASK (CPSID i)/ FAULTMASK (CPSID f ) register (set the register to 1)

## Slide 70
32-Bit 数据处理指令
指令 | 功能
ADC | 带进位加法
ADD | 加
ADDW | 宽加 (#immed_12)
AND | 逻辑与
ASR | 算术右移
BIC | 位清零 (一个值与另一个值的逻辑反转进行逻辑与)
BFC | 位域清零
CMP | 比较 (比较两个数据并更新标志)
CLZ | 计数前导0
EOR | 异或
LSL | 逻辑左移
LSR | 逻辑右移
MLA | 乘法累加
Notes: 32-Bit Data Processing Instructions
Instruction Function
ADC Add with carry
ADD Add
ADDW Add wide (#immed_12)
AND Logical AND
ASR Arithmetic shift right
BIC Bit clear (logical AND one value with the logic inversion of another value)
BFC Bit field clear
CMP Compare (compare two data and update flags)
CLZ Count lead zero
EOR Exclusive OR
LSL Logical shift left
LSR Logical shift right
MLA Multiply accumulate

## Slide 71
MSL | 乘和减
MOV | 传送
MVN | 传送取反的值
MUL | 乘
ORR | 逻辑或
ORN | 逻辑或非
RBIT | 保留位
REV | 字节保留字
ROR | 循环右移
RSB | 反向减法
RRX | 带扩展的循环右移
SBFX | 符号位域提取
SDIV | 符号除法
(Continued)
Notes: MSL Multiply and subtract
MOV Move
MVN Move negative
MUL Multiply
ORR Logical OR
ORN Logical OR NOT
RBIT Reverse bit
REV Byte reserve word
ROR Rotate right register
RSB Reverse subtract
RRX Rotate right extended
SBFX Signed bit field extract
SDIV Signed divide

## Slide 72
(Continued)
SMLAL | 带符号长乘加
SMULL | 带符号长乘
SSAT | 带符号饱和
SBC | 带借位减法
SUB | 减
SUBW | 宽减法(#immed_12)
SXTB | 符号扩展字节
TEQ | 测试等价(被用作逻辑异或; 标志会跟新但结果不会存储)
TST | 测试 (被用作逻辑与; Z 标志会更新但与的结果不会被存储)
UBFX | 无符号位域提取
USAT | 无符号饱和
UXTB | 无符号扩展字节
UXTH | 无符号扩展半字
Notes: SMLAL Signed multiply accumulate long
SMULL Signed multiply long
SSAT Signed saturate
SBC Subtract with carry
SUB Subtract
SUBW Subtract wide (#immed_12)
SXTB Sign extend byte
TEQ Test equivalent (use as logical exclusive OR; flags are updated but result is not stored)
TST Test (use as logical AND; Z flag is updated but AND result is not stored)
UBFX Unsigned bit field extract
USAT Unsigned saturate
UXTB Unsigned extend byte
UXTH Unsigned extend half word

## Slide 73
32-Bit 加载和存储指令
指令 | 功能
LDR | 从存储器向寄存器加载字
LDRB | 从存储器向寄存器加载字节
LDRH | 从存储器向寄存器加载半字
LDRSB | 从存储器中取字节，对它进行符号扩展，把它存入寄存器
LDRSH | 从存储器中取半字，对它进行符号扩展，把它存入寄存器
LDM | LDM 从存储器向寄存器加载多个数据
LDRD | LDRD 从存储器向寄存器加载双子数据
STR | STR 向存储器存储字
STM | 从寄存器向存储器存储多个字
STRD | 从寄存器向存储器存储双字数据
PUSH | Push 多个寄存器
POP | Pop 多个寄存器
Notes: 32-Bit Load and Store Instructions
Instruction Function
LDR Load word data from memory to register
LDRB Load byte data from memory to register
LDRH Load half word data from memory to register
LDRSB Load byte data from memory, sign extend it, and put it to register
LDRSH Load half word data from memory, sign extend it, and put it to register
LDM LDM Load multiple data from memory to registers
LDRD LDRD Load double word data from memory to registers
STR STR Store word to memory
STM Store multiple words from registers to memory
STRD Store double word data from registers to memory
PUSH Push multiple registers
POP Pop multiple registers

## Slide 74
32-Bit 分支指令
其他 32-Bit 指令
Instruction | Function
B | 分支
BL | 分支和连接
TBB | 分支字节表; 使用单字节偏移表向前分支
TBH | 半字分支表; 使用半字偏移表向前分支
指令 | 功能
LDREX | 独占加载字
STREX | 独占存储字
Notes: 32-Bit Branch Instructions
Instruction Function
B Branch
BL Branch and link
TBB Table branch byte; forward branch using a table of single byte offset
TBH Table branch half word; forward branch using a table of half word offset
Other 32-Bit Instructions
Instruction Function
LDREX Exclusive load word
STREX Exclusive store word

## Slide 75
(Continued)
CLREX | 清除本地处理器的独占访问记录
MRS | 移动专用寄存器到通用寄存器
MSR | 从通用寄存器移动到专用寄存器
NOP | 无操作
SEV | 发送事件
WFE | 事件睡眠和唤醒
WFI | 中断睡眠和唤醒
ISB | 指令同步隔离
DSB | 数据同步隔离
DMB | 数据存储器隔离
Notes: CLREX Clear the local exclusive access record of local processor
MRS Move special register to general-purpose register
MSR Move to special register from general-purpose register
NOP No operation
SEV Send event
WFE Sleep and wake for event
WFI Sleep and wake for interrupt
ISB Instruction synchronization barrier
DSB Data synchronization barrier
DMB Data memory barrier

## Slide 76
8.5.2 指令描述
8.5.2.1 汇编语言: 传送数据
数据传输可以是下列类型之一:
1. 在寄存器和寄存器间传送数据
2. 在存储器和寄存器间传送数据
3. 在专用寄存器和寄存器间传送数据
4. 把一个立即数传送给寄存器
Notes: 8.5.3 Instruction Descriptions
8.5.3.1 Assembler Language: Moving Data
Data transfers can be of one of the following types:
1. Moving data between register and register
2. Moving data between memory and register
3. Moving data between special register and register
4. Moving an immediate data value into a register

## Slide 77
通常使用的内存访问指令
访问存储器的基本指令是加载和存储
例子 | 描述
LDRB Rd, [Rn, #offset] | 从存储器位置 Rn + offset 读取字节
LDRH Rd, [Rn, #offset] | 从存储器位置 Rn + offset 读取半字
LDR Rd, [Rn, #offset] | 从存储器位置 Rn + offset 读取字
LDRD Rd1,Rd2, [Rn, #offset] | 从存储器位置 Rn + offset 读取双字
STRB Rd, [Rn, #offset] | 向存储器位置 Rn + offset 存储字节
STRH Rd, [Rn, #offset] | 向存储器位置 Rn + offset 存储半字
STR Rd, [Rn, #offset] | 向存储器位置 Rn + offset 存储字
STRD Rd1,Rd2, [Rn, #offset] | 向存储器位置 Rn + offset 存储双字
Notes: The basic instructions for accessing memory are Load and Store.
Commonly Used Memory Access Instructions
Example Description
LDRB Rd, [Rn, #offset] Read byte from memory location Rn + offset
LDRH Rd, [Rn, #offset] Read half-word from memory location Rn + offset
LDR Rd, [Rn, #offset] Read word from memory location Rn + offset
LDRD Rd1,Rd2, [Rn, #offset] Read double word from memory location Rn + offset
STRB Rd, [Rn, #offset] Store byte to memory location Rn + offset
STRH Rd, [Rn, #offset] Store half word to memory location Rn + offset
STR Rd, [Rn, #offset] Store word to memory location Rn + offset
STRD Rd1,Rd2, [Rn, #offset] Store double word to memory location Rn + offset

## Slide 78
多重加载和存储操作:LDM (加载多个); STM (存储多个)
多个内存访问指令
例子 | 描述
LDMIA Rd!, <reg list> | 从 Rd 指定的存储位置读取多个字
STMIA Rd!, <reg list> | 从 Rd 指定的存储位置存储多个字
LDMIA.W Rd!, <reg list> | 从 Rd 指定的存储位置读取多个字
LDMDB.W Rd!, <reg list> | 从 Rd 指定的存储位置读取多个字
STMIA.W Rd!, <reg list> | 从 Rd 指定的存储位置写多个字
STMDB.W Rd!, <reg list> | 从 Rd 指定的存储位置写多个字
Notes: Multiple Load and Store operations:
LDM (Load Multiple); STM (Store Multiple).
Multiple Memory Access Instructions
Example Description
LDMIA Rd!, <reg list> Read multiple words from memory location specified by Rd.
STMIA Rd!, <reg list> Store multiple words to memory location specified by Rd.
LDMIA.W Rd(!),<reg list> Read multiple words from memory location specified by Rd.
LDMDB.W Rd(!), <reg list> Read multiple words from memory location specified by Rd.
STMIA.W Rd(!), <reg list> Write multiple words to memory location specified by Rd.
STMDB.W Rd(!), <reg list> Write multiple words to memory location specified by Rd.

## Slide 79
通常一条 PUSH 指令会有相同寄存器列表的相应的POP指令 , 但是这并不总是必须的。
PUSH {R0-R3, LR} ; Save register contents at beginning of subroutine
.... ; Processing
POP {R0-R3, PC} ; restore registers and return
传送立即数到寄存器:
MOV R0, #0x12 ; Set R0 to 0x12
对于大的取值(超过 8 比特), 你可能需要使用一条 Thumb-2 传送指令。
MOVW.W R0, #0x789A ; Set R0 to 0x789A
Notes: Usually a PUSH instruction will have a corresponding POP with the same register list, but this is not always necessary.
PUSH {R0-R3, LR} ; Save register contents at beginning of subroutine
.... ; Processing
POP {R0-R3, PC} ; restore registers and return
Moving immediate data into a register:
MOV R0, #0x12 ; Set R0 to 0x12
For a larger value (over 8 bits), you might need to use a Thumb-2 move instruction.
MOVW.W R0,#0x789A ; Set R0 to 0x789A

## Slide 80
你也可以使用LDR (在ARM汇编中使用的一条伪指令):
LDR R0, =0x3456789A
这并不是一条真正的汇编命令, 但是ARM的汇编器会把它转换成一条PC相关的加载指令来产生需要的数据。
对于 LDR, 如果地址是一个程序地址值, 它会自动把LSB为设为1。
LDR R0, =address1 ; R0 set to 0x4001
...
address1
0x4000: MOV R0, R1 ; address1 contains program code
...
Notes: You can also use LDR (a pseudo instruction provided in ARM assembler):
LDR R0, =0x3456789A
This is not a real assembler command, but the ARM assembler will convert it into a PC relative load instruction to produce the required data.
For LDR, if the address is a program address value, it will automatically set the LSB to 1.
LDR R0, =address1 ; R0 set to 0x4001
...
address1
0x4000: MOV R0, R1 ; address1 contains program code
...

## Slide 81
8.5.3.2 汇编语言: 数据处理
例: ADD
ADD R0, R1 ; R0 = R0 + R1
ADD R0, #0x12 ; R0 = R0 + 0x12
ADD.W R0, R1, R2 ; R0 = R1 + R2
当代码中使用16位指令时，ADD指令改变PSR的相应标志位。
ADD.W R0, R1, R2 ; Flag unchanged
ADDS.W R0, R1, R2 ; Flag change
Notes: 8.5.3.2 Assembler Language: Processing Data
Many data operation instructions can have multiple instruction formats.
Example: ADD
ADD R0, R1 ; R0 = R0 + R1
ADD R0, #0x12 ; R0 = R0 + 0x12
ADD.W R0, R1, R2 ; R0 = R1 + R2
When 16-bit Thumb code is used, an ADD instruction changes the flags in the PSR.
ADD.W R0, R1, R2 ; Flag unchanged
ADDS.W R0, R1, R2 ; Flag change

## Slide 82
指令 | 操作
ADD Rd, Rn, Rm ; Rd = Rn + Rm ADD Rd, Rm ; Rd = Rd + Rm ADD Rd, #immed ; Rd = Rd + #immed | 加法
ADC Rd, Rn, Rm ; Rd = Rn + Rm + carry ADC Rd, Rm ; Rd = Rd + Rm + carry ADC Rd, #immed ; Rd = Rd + #immed + carry | 带进位的加法
ADDW Rd, Rn,#immed ; Rd = Rn + #immed | 寄存器与12位立即数相加
SUB Rd, Rn, Rm ; Rd = Rn – Rm SUB Rd, #immed ; Rd = Rd – #immed SUB Rd, Rn,#immed ; Rd = Rn –#immed | 减法
RSB.W Rd, Rn, #immed ; Rd = #immed –Rn RSB.W Rd, Rn, Rm ; Rd = Rm - Rn MUL Rd, Rm ; Rd = Rd * Rm Multiply MUL.W Rd, Rn, Rm ; Rd = Rn * Rm | 反向减法
UDIV Rd, Rn, Rm ; Rd = Rn /Rm SDIV Rd, Rn, Rm ; Rd = Rn /Rm | 无符号、有符号除法
Notes: Examples of Arithmetic Instructions
Instruction Operation
ADD Rd, Rn, Rm ; Rd = Rn + Rm
ADD Rd, Rm ; Rd = Rd + Rm
ADD Rd, #immed ; Rd = Rd + #immed ADD operation
ADC Rd, Rn, Rm ; Rd = Rn + Rm + carry
ADC Rd, Rm ; Rd = Rd + Rm + carry
ADC Rd, #immed ; Rd = Rd + #immed + carry ADD with carry
ADDW Rd, Rn,#immed ; Rd = Rn + #immed ADD register with 12-bit immediate value
SUB Rd, Rn, Rm ; Rd = Rn – Rm
SUB Rd, #immed ; Rd = Rd – #immed
SUB Rd, Rn,#immed ; Rd = Rn –#immed SUBTRACT
RSB.W Rd, Rn, #immed ; Rd = #immed –Rn
RSB.W Rd, Rn, Rm ; Rd = Rm - Rn
MUL Rd, Rm ; Rd = Rd * Rm Multiply
MUL.W Rd, Rn, Rm ; Rd = Rn * Rm Reverse subtract
UDIV Rd, Rn, Rm ; Rd = Rn /Rm
SDIV Rd, Rn, Rm ; Rd = Rn /Rm Unsigned and signed divide

## Slide 83
8.5.3.3 汇编语言: 子程调用和无条件跳转
最基本的分支指令如下:
B label ; 跳转到label所指向的分支
BX reg ; 跳转到reg寄存器所指向的地址
在BX 指令中, 寄存器的LSB=1，表示Thumb状态。
调用一个函数:
BL label ; 跳转到label指向的地址并且在LR中保存返回
；地址
BLX reg ;跳转到reg寄存器所指向的地址并且
;在LR中保存返回地址.
Notes: 8.5.3.3 Assembler Language: Call and Unconditional Branch
The most basic branch instructions are:
B label ; Branch to a labeled address
BX reg ; Branch to an address specified by a register
In BX instructions, the LSB of the value contained in the register determines the next state of the processor.
To call a function:
BL label ; Branch to a labeled address and save return address in LR
BLX reg ; Branch to an address specified by a register and
; save return address in LR.

## Slide 84
8.5.3.4 汇编语言: 判断和条件分支
在APSR中， 有五个标志位；其中四个用作条件分支选择.
Flag bits in APSR That Can Be Used for Conditional Branches
标志 | PSR 位 | 描述
N | 31 | Negative flag (上次运算结果是否为负标志)
Z | 30 | Zero (上次运算结果是否为0标志)
C | 29 | Carry (进位或借位标志)
V | 28 | Overflow (运算结果越界标志)
Notes: 8.5.3.4 Assembler Language: Decisions and Conditional Branches
In the APSR, there are five flag bits; four of them are used for branch decisions.
Flag bits in APSR That Can Be Used for Conditional Branches
Flag PSR Bit Description
N 31 Negative flag (last operation result is a negative value)
Z 30 Zero (last operation result returns a zero value)
C 29 Carry (last operation returns a carry out or borrow)
V 28 Overflow (last operation results in an overflow)

## Slide 85
通过4个标志的组合(N, Z, C, V)，一共定义了15个条件分支
Conditions for Branches or Other Conditional Operations
符号 | 条件 | 标志
EQ | Equal | Z set
NE | Not equal | Z clear
CS/HS | Carry set/unsigned higher or same | C set
CC/LO | Carry clear/unsigned lower | C clear
MI | Minus/negative | N set
PL | Plus/positive or zero | N clear
VS | Overflow | V set
VC | No overflow | V clear
HI | Unsigned higher | C set and Z clear
LS | Unsigned lower or same | C clear or Z set
Notes: With combinations of the four flags (N, Z, C, and V), 15 branch conditions are defined.
Conditions for Branches or Other Conditional Operations
Symbol Condition Flag
EQ Equal Z set
NE Not equal Z clear
CS/HS Carry set/unsigned higher or same C set
CC/LO Carry clear/unsigned lower C clear
MI Minus/negative N set
PL Plus/positive or zero N clear
VS Overflow V set
VC No overflow V clear
HI Unsigned higher C set and Z clear
LS Unsigned lower or same C clear or Z set
85

## Slide 86
例:
BEQ label ; 如果Z标志位为1，则跳转到地址’label’
Thumb-2 version
BEQ.W label ;如果Z标志位为1，则跳转到地址’label’
(续)
LT | Signed less than | N set and V clear, or N clear and V set (N != V)
GT | Signed greater than | Z clear, and either N set and V set, or N clear and V clear (Z == 0, N == V)
LE | Signed less than or equal | Z set, or N set and V clear, or N clear and V set (Z == 1 or N != V)
AL | Always (unconditional) | —
Notes: Example:
BEQ label ; Branch to address ‘label’ if Z flag is set
Thumb-2 version
BEQ.W label ; Branch to address ‘label’ if Z flag is set
86

## Slide 87
8.5.4 Cortex-M3中一些有用的指令
MRS 和MSR
访问一些特殊寄存器
MRS <Rn>, <SReg> ; 从特殊寄存器读出
MSR <SReg>, <Rn> ; 向特殊寄存器写入
MRS和MER可以访问的特殊寄存器名
符号 | 描述
IPSR | 中断状态寄存器
EPSR | 执行状态寄存器
APSR2 | 以前操作标志
IEPSR | IPSR和EPSR组合
IAPSR | IPSR和APSR组合
Notes: Special Register Names for MRS and MSR Instructions
Execution status register (read as zero)
Flags from previous operation
A composite of IPSR and EPSR
A composite of IPSR and APSR
87

## Slide 88
Example:
LDR R0, =0x20008000 ; 为程序堆栈指针赋新值(PSP)
MSR PSP, R0
EAPSR | EPSR和APSR组合
PSR | EPSR、IPSR和APSR组合
MSP | 主堆栈指针
PSP | 进程堆栈指针
PRIMASK | 正常的异常屏蔽寄存器
BASEPRI | 正常的异常优先级屏蔽寄存器
BASEPRI_MAX | 带条件写的正常的异常优先级屏蔽寄存器 (新的优先级必须高于旧的优先级)
FAULTMASK | 错误异常屏蔽寄存器(同时屏蔽正常的中断)
CONTROL | 控制寄存器
(续)
Notes: A composite of EPSR and APSR
A composite of APSR, EPSR and IPSR
Main stack pointer
Process stack pointer
Normal exception mask register
Normal exception priority mask register
Same as normal exception priority mask register, with conditional write (new priority level must be higher than the old level)
Fault exception mask register (also disables normal interrupts)
Control register
88

## Slide 89
8.6 典型安装
在典型的程序中，你需要考虑一系列区域:
1. 代码区域:
1) 特权代码，包括启动向量表
2) 用户代码
2. SRAM 区域:
1) 特权数据，包括主堆栈
2) 用户数据，包括进程堆栈
3) 特权位带别名区
4) 用户位带别名区
Notes: In typical applications, you need to consider a number of regions:
1. Code region:
1) Privileged code, including a starting vector table
2) User code
2. SRAM region:
1) Privileged data, including the main stack
2) User data, including the process stack
3) Privileged bit-band alias region
4) User bit-band alias region
89

## Slide 90
3. 外设:
1) 特权外设
2) 用户外设
3) 特权外设位带别名区
4) 用户外设位带别名区
4. 系统控制空间(NVIC and debug components):
1) 只有特权访问
Notes: 1) Privileged peripherals
2) User peripherals
3) Privileged peripheral bit-band alias region
4) User peripheral bit-band alias region
. System Control Space (NVIC and debug components):
1) Privileged accesses only
90

## Slide 91
- THE END -