## Slide 1: 第九章
Cortex-M3 异常和中断
Notes: Chapter 9
Cortex-M3 Exceptions and Interrupt
1

## Slide 2
9.1 异常
9.1.1 异常类型
异常是 编号为1到15的系统异常，而余下的240个是外部中断输入。（向量表中共256条）
异常是另一种形式的中断，它是由内部错误引起的，或者内核的SysTick、SVCall等。而中断是由随机的外部事件引发的。
大部分的异常可编程优先级，其中很少的一些有固定的优先级。
当前运行的异常值，是由特殊寄存器IPSR​​或NVIC的中断控制状态寄存器表示的。
Notes: Exceptions are numbered 1 to 15 for system exceptions and the rest 240 for external interrupt inputs.(Total 256 entries in vector table.)
Exception is another form of interrupt which is arosed by the internal fault, SysTick, SVCall,etc within the core. But interrupt is invoked by random external event.
Most of the exceptions have programmable priority, and a few have fixed priority.
The value of the current running exception is indicated by the special register IPSR or from the NVIC’s Interrupt Control State Register.
2

## Slide 3
异常表
异常号 | 异常类型 | 优先级 | 描述
1 | 复位 | -3 (最高) | 复位
2 | NMI | 2 | 不可屏蔽中断(外部NMI 输入)
3 | 硬件错误 | -1 | 各种错误情况
4 | 内存管理错误 | 可编程 | 内存管理错误； MPU 访问非法地址
5 | 总线错误 | 可编程 | 总线错误，比如预取终止
6 | 使用错误 | 可编程 | 由于程序错误或尝试访问协处理器导致的异常
7-10 | 保留 | N/A | —
11 | SVCall | 可编程 | 系统服务调用
12 | 调试监视器 | 可编程 | 调试监视器
Notes: Exception Type
Priority
Description
Reset
-3 (Highest)
Reset
NMI
2
Nonmaskable interrupt (external NMI input)
Hard Fault
-1
All fault conditions, if the corresponding fault handler is not enabled
MemManage Fault
Programmable
Memory management fault; MPU violation or access to illegal locations
Bus Fault
Programmable
Bus error, like Prefetch abort
Usage Fault
Programmable
Exceptions due to program error or trying to access coprocessor
Reserved
N/A
—
SVCall
Programmable
System Service call
Debug Monitor
Programmable
Debug monitor
3

## Slide 4
当一个被使能的异常发生时，如果它不能够被立即执行，它将被挂起。
13 | 保留 | N/A | —
14 | PendSV | 可编程 | 可挂起系统设备申请
15 | SYSTICK | 可编程 | 系统时钟定时器
16 | 外部中断#0 | 可编程 | 外部中断
17 | 外部中断#1 | 可编程 | 外部中断
… | … | … | …
255 | 外部中断#239 | 可编程 | 外部中断
(续)
Notes: 14
PendSV
Programmable
Pendable request for system device
15
SYSTICK
Programmable
System Tick Timer
16
External Interrupt #0
Programmable
External Interrupt
17
External Interrupt #1
Programmable
External Interrupt
…
…
…
…
255
External Interrupt #239
Programmable
External Interrupt
4

## Slide 5
9.1.2 优先级定义
异常的优先级:
一个高优先级的异常可以抢占一个低优先级的异常.
复位, NMI, 和硬件错误有特定的优先级.
Cortex-M3 支持256级可编程异常.
减少优先级数可以通过减少优先级配置寄存器的一些低位来实现。
Notes: 一个高优先级的异常可以抢占一个低优先级的异常.
A higher-priority exception can preempt(抢占) a lower-priority exception.
Reset, NMI, and hard fault have fixed priority levels.
The Cortex-M3 supports 256 levels of programmable priority.
The reduction of priority levels can be implemented by cutting out several lowest bits of the priority configuration registers.
5

## Slide 6
3 比特优先级
4比特优先级
优先级寄存器的最小宽度值为3比特.
Bit 7 | Bit 6 | Bit 5 | Bit 4 | Bit 3 | Bit 2 | Bit 1 | Bit 0
使用 |  |  | 不使用, 读出值为0 |  |  |  | 
Bit 7 | Bit 6 | Bit 5 | Bit 4 | Bit 3 | Bit 2 | Bit 1 | Bit 0
使用 |  |  |  | 不使用, 读出值为0 |  |  | 
Notes: The minimum number of implemented priority register widths is 3 bits.
6

## Slide 7
3位或4位宽度的可用优先级
Notes: Available Priority Levels with 3-Bit or 4-Bit Priority Width
7

## Slide 8
3 位、5 位和8 位表达优先级时，优先级寄存器的使用情况
优先级 | 异常类型 | 3比特优先级寄存器的设备 | 5比特优先级寄存器的设备 | 8比特优先级寄存器的设备
-3 (Highest) | 复位 | -3 | -3 | -3
-2 | NMI | -2 | -2 | -2
-1 | 硬件错误 | -1 | -1 | -1
0, | 具有优先级并且可编程的异常 | 0x00 | 0x00 | 0x00, 0x01
1, |  | 0x20 | 0x08 | 0x02, 0x03
… |  | … | … | …
0xFF |  | 0xE0 | 0xF8 | 0xFE, 0xFF
Notes: Available Priority Levels for
Devices with 3-bit, 5-bit, and 8-bit Priority Level Registers
8

## Slide 9
该8比特寄存器可以进一步分为2部分: 抢占优先和次优先。
抢占优先级和子优先级的表达，位数与分组位置的关系
优先组 | 抢占优先级字段 | 子优先级字段
0 | Bit [7:1] | Bit [0]
1 | Bit [7:2] | Bit [1:0]
2 | Bit [7:3] | Bit [2:0]
3 | Bit [7:4] | Bit [3:0]
4 | Bit [7:5] | Bit [4:0]
5 | Bit [7:6] | Bit [5:0]
6 | Bit [7] | Bit [6:0]
7 | None | Bit [7:0]
Notes: The 8-bit register is further divided into two parts: preempt priority and subpriority.
For each exception with programmable priority levels, the register is divided into two halves. The upper half and the lower half.
Definition of Preempt Priority Field and Subpriority Field in a Priority Level Register in Different Priority Group Settings
9

## Slide 10
应用程序中断及复位控制寄存器(AIRCR) （地址：0xE000_ED0 0 ）
Bits | 名 | 类型 | 复位值 | 描述
31:16 | VECTKEY | R/W | — | 存取关键字；为了写入这个寄存器必须向这个地址写人 0x05FA
15 | ENDIANNESS | R | — | 表示数据的排列顺序： 1 表示大端(BE8) 而0表示小端
10:8 | PRIGROUP | R/W | 0 | 优先组
2 | SYSRESETREQ | W | — | 请求芯片控制逻辑产生一个复位信号
1 | VECTCLRACTIVE | W | — | 清除异常的所有活跃状态信息
0 | VECTRESET | W | — | 复位Cortex-M3 处理器。 但不会复位处理器以外的电路。
Notes: Application Interrupt and Reset Control Register (Address 0xE000ED0C)
Access key; 0x05FA must be written to this field to write to this register
Indicates endianness for data: 1 for big endian (BE8) and 0 for little endian
Priority group
Requests chip control logic to generate a reset
Clears all active state information for exceptions
Resets the Cortex-M3 processor, but this will not reset circuits outside the processor
10

## Slide 11
配置寄存器的宽度 | 3 | 3
优先组 | 5 | 1
抢占优先级 | 4 | 8
次优先级 (在每个抢占优先级内部) | 2 | —
Bit 7 | 抢占优先级 | 抢占优先级[5:3]
Bit 6 |  | 
Bit 5 | 次优先级 | 
Bit 4 |  | 抢占优先级bit[2:0] (总是0)
Bit 3 |  | 
Bit 2 |  | 
Bit 1 |  | 次优先级(总是0)
Bit 0 |  | 
优先组设置的例子
Notes: priority group
preempt priority levels
Subpriority levels (inside each preempt level)
Preempt Priority
Sub priority
Preempt Priority[5:3]
Preempt Priority bit[2:0] (always 0)
Subpriority (always 0)
11

## Slide 12
9.1.3 向量表
当发生了异常并且要响应它时，CM3 需要定位其服务例程的入口地址。这些入口地址存储在所谓的“（异常）向量表”中。缺省情况下，CM3 认为该表位于零地址处，且各向量占用 4 字节。
上电后的异常向量表
地址 | 异常号 | 值(大小为“字”)
0x00000000 | — | MSP 初始值
0x00000004 | 1 | 复位向量(程序计数器初始值)
0x00000008 | 2 | NMI 句柄启动地址
0x0000000C | 3 | 硬件错误句柄启动地址
… | … | 其它句柄启动地址
Notes: The processor will need to locate the starting address of the exception handler when an exception is being handled. This information is stored in the vector table.
复位向量(program counter initial value)
NMI handler starting address
Hard fault handler starting address
Other handler starting address
12

## Slide 13
通过设置NVIC中的向量表偏移寄存器，可以将向量表重定位到其它的内存地址
该地址偏移需要与向量表的大小对齐， 扩展到2的若干次幂
例:
IRQ 输入: 32
总异常数： 32 + 16 (system exceptions) = 48
扩展到2的幂: 64.
乘以4: 256.
向量表地址偏移可以被编程为0x0, 0x100, 0x200等等。
Notes: The vector table can be relocated to other memory locations, done by setting the vector table offset register in the NVIC.
The address offset should be aligned to the vector table size, extended to the power of 2.
Example:
IRQ inputs: 32
The total number of exceptions: 32 + 16 (system exceptions) = 48
Extending it to the power of 2: 64.
Multiplying it by 4: 256.
The vector table offset can be programmed as 0x0, 0x100, 0x200, and so on.
13

## Slide 14
如果需要动态地更改向量表，则对于任何器件来说，向量表的起始处都必须包含以下向量：
1. 初始化主堆栈指针
2. 复位向量
3. NMI 向量
4. 硬件错误向量
向量表偏移寄存器(地址0xE000ED08)
Bits | 名 | 类型 | 复位值 | 描述
29 | TBLBASE | R/W | 0 | 表基地址在Code (0) 或RAM (1)
28:7 | TBLOFF | R/W | 0 | 来自CODE区或RAM区的表偏移范围
Notes: 表基地址在Code (0) 或RAM (1)
Table base in Code (0) 或RAM (1)
To allow dynamic changing of exception handlers, in the beginning of the boot image you need to have these (at a minimum):
1. Initial Main Stack Pointer value
2. Reset vector
3. NMI vector
4. Hard fault vector
14

## Slide 15
9.1.4 中断输入和挂起行为
当中断输入脚被置为有效后，该中断就被悬起。即使后来中断源撤消了中断请求，已经被标记成悬起的中断也被记录下来。到了系统中它的优先级最高的时候，就会得到响应。
中断挂起
Notes: When an interrupt input is asserted, it will be pended.
Even if the interrupt source de-asserts the interrupt, the pended interrupt status will still cause the interrupt handler to be executed.
15

## Slide 16
如果在某个中断得到响应之前，其悬起状态被清除了（例如，在PRIMASK 或FAULTMASK置位的时候软件清除了悬起状态标志），则中断被取消
在处理器执行前，中断挂起被清除
Notes: If the pending status is cleared before the processor starts responding to the pended interrupt.
Interrupt Pending Cleared Before Processor Takes Action
16

## Slide 17
当某中断的服务例程开始执行时，就称此中断进入了“活跃”状态，并且其悬起位会被硬件自动清除。在一个中断活跃后，直到其服务例程执行完毕，并且返回后，才能对该中断的新请求予以响应。
处理器进入服务例程后对中断活跃状态的设置
Notes: When the processor starts to execute an interrupt, the interrupt becomes active and the pending bit will be cleared automatically.
Interrupt Active Status Set as Processor Enters Handler
17

## Slide 18
如果中断源咬住请求信号不放，该中断就会在其上次服务例程返回后再次被置为悬起状态.
在中断结束后，连续中断请求再次挂起
Notes: If an interrupt source continues to hold the interrupt request signal active, the interrupt will be pended again at the end of the interrupt service routine.
Continuous Interrupt Request Pends Again After Interrupt Exit
18

## Slide 19
如果一个中断在处理器执行前有多次脉冲，它将被视为一次中断请求，而不是多次。
中断请求过快导致一部分请求错失的情况
Notes: If an interrupt is pulsed several times before the processor starts processing it, it will be treated as one single interrupt request.
Interrupt Pending Only Once, Even with Multiple Pulses Before the Handler
19

## Slide 20
如果在服务例程执行时，中断请求释放了，但是在服务例程返回前又重新被置为有效，则 CM3会记住此动作，重新悬起该中断。
在执行ISR 时中断悬起再次发生
Notes: If an interrupt is de-asserted and then pulsed again during the interrupt service routine, it will be pended again.
Interrupt Pending Occurs Again During the Handler
20

## Slide 21
9.1.5 Fault 类异常
9.1.5.1 总线faults
当AHB 接口上正在传送数据时，如果回复了一个错误信号 ，则会产生总线faults，产生的场合可以是：
1. 取指令
2. 数据读/写
3. 中断进程开始的压栈
4. 中断进程结束时的出栈
5.处理器启动中断服务序列后读取向量
Notes: 9.1.5 Fault Exceptions
9.1.5.1 Bus faults
Bus faults are produced when an error response is received during a transfer on the AHB interfaces.
Bus fault can happen at:
1. Instruction fetch
2. Data read/write
3. Stack PUSH in the beginning of interrupt processing
4. Stack POP at the end of interrupt processing
5. Reading of an interrupt vector address when the processor starts the interrupt-handling sequence.
21

## Slide 22
当这些类型的总线faults发生时,
If
1. 该总线faults使能.
2. 没有其它相同优先级的异常在运行.
Then
该总线faults被执行.
Else if
同时处理器接收另一个更高优先级的异常.
Then
总线故障的异常将被挂起.
Notes: When these types of bus faults take place,
If
1. The bus fault handler is enabled.
2. No other exceptions with the same or higher priority are running.
Then
The bus fault handler will be executed.
Else if
At the same time the core receives another exception handler with higher priority.
Then
The bus fault exception will be pending.
In some special cases, the hard fault handler will be executed or the core will enter a lockup state.
22

## Slide 23
NVIC 有一些错误状态寄存器. 其中一个就是总线fault状态寄存器 (BFSR).
总线fault 状态寄存器(BFSR)，地址：0xE000_ED29
Bits | 名 | 类型 | 复位值 | 描述
7 | BFARVALID | — | 0 | 表示BFAR 无效
6:5 | — | — | — | —
4 | STKERR | R/Wc | 0 | 入栈错误
3 | UNSTKERR | R/Wc | 0 | 出栈错误
2 | IMPREISERR | R/Wc | 0 | 不精确的数据访问冲突
1 | PRECISERR | R/Wc | 0 | 精确的数据访问冲突
0 | IBUSERR | R/Wc | 0 | 指令访问冲突
Notes: The NVIC has a number of fault status registers. One of them is the Bus Fault Status Register (BFSR).
Stacking error
Unstacking error
Imprecise data access violation
Precise data access violation
Instruction access violation
23

## Slide 24
9.1.5.2 存储器管理faults
存储器管理faults常见诱因：
访问了所有MPU regions 覆盖范围之外的地址
访问了没有存储器与之对应的空地址
往只读region写数据
用户级下访问了只允许在特权级下访问的地址
Notes: Common memory manage faults include:
1. Access to memory regions not defined in MPU setup.
2. Execute code from nonexecutable memory regions.
3. Writing to read-only regions.
4. An access in the user state to a region defined as privileged access only.
24

## Slide 25
当这些存储器管理fault发生时，
if
1. 如果存储器管理fault服务例程使能
2. 没有其他相同或更高优先级异常在运行
Then
存储器管理fault服务例程将被执行。
Else if
同时，处理器接受另一个具有更高优先级的异常。
Then
存储器管理fault异常将被挂起。
Notes: When a memory manage faults occurs,
if
1. The memory manage fault handler is enabled.
2. No other exceptions with the same or higher priority are running.
Then
The memory manage fault handler will be executed.
Else if
At the same time the core receives another exception handler with higher priority.
Then
The memory manage fault exception will be pending.
In some special cases, the hard fault handler will be executed or the core will enter a lockup state.
25

## Slide 26
NVIC 有一个存储器管理fault状态寄存器(MFSR) 来映射存储器管理fault的情况。
存储器管理fault 状态寄存器(MFSR) ，地址：0xE000_ED28
Bits | 名 | 类型 | 复位值 | 描述
7 | MMARVALID | — | 0 | 说明MMAR 是有效地
6:5 | — | — | — | —
4 | MSTKERR | R/Wc | 0 | 入栈错误
3 | MUNSTKERR | R/Wc | 0 | 出栈错误
2 | — | — | — | —
1 | DACCVIOL | R/Wc | 0 | 数据访问失败
0 | IACCVIOL | R/Wc | 0 | 指令访问失败
Notes: The NVIC contains a Memory Management Fault Status Register (MFSR) to indicate the cause of the memory management fault.
26

## Slide 27
9.1.5.3 用法faults
可以引起用法faults的有：
1. 未定义指令
2. 协处理器指令
3. 尝试转换到ARM状态
4. 无效中断返回(链接寄存器包括无效/不正确的数值)
5. 使用多重加载或存储指令访问非对齐地址
通过设置NVIC中的某些位， 产生下列用法faults:
除以0
任何非对齐内存访问
Notes: 9.1.5.3 Usage Faults
Usage faults can be caused by:
1. Undefined instructions
2. Coprocessor instructions
3. Trying to switch to the ARM state
4. Invalid interrupt return (Link Register contains invalid/incorrect values)
5. Unaligned memory accesses using multiple load or store instructions
By setting up certain control bits in the NVIC, to generate usage faults for:
1. Divide by zero
2. Any unaligned memory accesses
27

## Slide 28
当一个用法fault产生时，
if
1. 用法faults服务例程使能。
2. 没有相同或更高优先级的异常运行。
Then
用法fault服务例程将被执行。
Else if
同时处理器接收另一个更高优先级的异常。
Then
用法fault异常将被挂起。
Notes: if
1. The usage fault handler is enabled.
2. No other exceptions with the same or higher priority are running.
Then
The usage fault handler will be executed.
Else if
At the same time the core receives another exception handler with higher priority.
Then
The usage fault exception will be pending.
In some special cases, the hard fault handler will be executed or the core will enter a lockup state.
28

## Slide 29
NVIC提供一个用法fault状态寄存器 (UFSR) 使得用法fault服务例程能够确定fault的原因。
用法fault 状态寄存器( U FSR)，地址：0xE000_ED2 A
Bits | 名 | 类型 | 复位值 | 描述
9 | DIVBYZERO | R/Wc | 0 | 表明出现了除以0的错误 (仅当DIV_0_TRP 置位有效)
8 | UNALIGNED | R/Wc | 0 | 表明访问一个地址非对齐区域的错误
7:4 | — | — | — | —
3 | NOCP | R/Wc | 0 | 尝试执行一个协处理器指令
2 | INVPC | R/Wc | 0 | 尝试去处理一个有错误返回值的异常
1 | INVSTATE | R/Wc | 0 | 尝试切换到无效状态(e.g., ARM)
0 | UNDEFINSTR | R/Wc | 0 | 尝试去执行没有定义的指令
Notes: The NVIC provides a Usage Fault Status Register (UFSR) for the usage fault handler to determine the cause of the fault.
Indicates that an unaligned access fault has taken place
—
Attempts to execute a coprocessor instruction
Attempts to do an exception with a bad value in the EXC_RETURN number
Attempts to switch to an invalid state (e.g., ARM)
Attempts to execute an undefined instruction
29

## Slide 30
9.1.5.4 硬fault
引起硬fault的有：
1. 用法faults，总线faults，存储器管理faults
2. 取向量期间的总线fault
硬fault 状态寄存器（地址：0xE000_ED2C）
Bits | 名 | 类型 | 复位值 | 描述
31 | DEBUGEVT | R/Wc | 0 | 表示硬件错误是由调试事件触发的的
30 | FORCED | R/Wc | 0 | 表示硬件错误是由总线错误，内存管理错误或用法错误引起的
29:2 | — | — | — | —
1 | VECTBL | R/Wc | 0 | 表明硬件错误是由总线错误期间的获取向量引起的
0 | — | — | — | —
Notes: 1. Usage faults, bus faults, and memory management faults
2. A bus fault during vector fetch
Indicates hard fault is triggered by debug event
Indicates hard fault is taken because of bus fault, memory management fault, or usage fault
—
Indicates hard fault is caused by failed vector fetch
30

## Slide 31
9.1.5.5 处理错误
在一个真实运行的系统中，在检查到错误的原因后，软件需要决定下一步要做什么。
一些错误处理办法：
1. 复位:
使用在NVIC中的应用程序中断和复位控制寄存器里的VECTRESET 控制位 (复位处理器但不是整个芯片)。
2. 覆盖:
重新解决引发错误异常的问题也是有可能的。
3. 任务终止:
对操作系统上运行的系统， 如果需要的话可将引发错误的任务终止并重启。
Notes: 9.1.5.5 Dealing with Faults
In a real running system, After the cause of a fault is determined, the software will have to decide what to do next.
Some fault-handling methods:
1. Reset:
Using the VECTRESET control bit in the Application Interrupt and Reset Control register in the NVIC (reset the processor but not the whole chip).
2. Recover:
It is possible to resolve the problem that caused the fault exception.
3. Task termination:
For systems running an OS, it is likely that the task that caused the fault will be terminated and restarted if needed.
31

## Slide 32
9.1.6 SVC 和PendSV
SVC （系统服务调用，亦简称系统调用）和 PendSV（可悬起系统调用），多用在上了操作系统的软件开发中。
9.1.6.1 SVC
SVC 用来产生系统函数调用。
例:
操作系统可以通过SVC提供硬件访问，而不是允许用户程序直接访问硬件。
SVC 可以提高软件的可移植性，因为用户程序无需知道硬件的编程细节。
Notes: 9.1.6 SVC and PendSV
SVC (System Service Call) and PendSV (Pended System Call) are two exceptions targeted at software and operating systems.
9.1.6.1 SVC
SVC is for generating system function calls.
Example:
Instead of allowing user programs to directly access hardware, operating system may provide access to hardware via an SVC.
SVC can make software more portable because the user application does not need to know the programming details of the hardware.
32

## Slide 33
例:
SVC 0x3 ; Call SVC function 3
SVC as a Gateway for OS Functions

## Slide 34
9.1.6.2 PendSV
PendSV (挂起系统调用) 可以被挂起，并且OS 通过挂起一个异常来保证一个动作在另一个很重要的任务完成后再执行。
PendSV一个典型的用途是 上下文切换(不同任务的切换)。
例:
假设有这么一个系统，里面有两个就绪的任务，并且通过
SysTick 异常启动上下文切换。
若在产生SysTick 异常时正在响应一个中断，则SysTick 异常会抢占其ISR 。
Notes: 9.1.6.2 PendSV
PendSV (挂起系统调用) works with SVC in the OS. PendSV can be pended and is useful for an OS to pend an exception so that an action can be performed after other important tasks are completed.
A typical use of PendSV is context switching (switching between tasks).
Example:
A system with only two tasks, and a context switch is triggered by SYSTICK exceptions.
If an interrupt request takes place before the SYSTICK exception, the SYSTICK exception will preempt the IRQ handler.
34

## Slide 35
两个任务间通过 SysTick 进行轮转调度的简单模式
Notes: Some OS implementations carry out only context switching if they detect that none of the IRQ handlers are being executed.
35

## Slide 36
发生IRQ 时上下文切换的问题
Notes: PendSV exception solves the problem by delaying the context-switching request until all other IRQ handlers have completed their processing.
36

## Slide 37
使用PendSV 控制上下文切换

## Slide 38
任务A 呼叫SVC 来请求任务切换（例如，等待某些工作完成）
OS接收到请求，做好上下文切换的准备，并且悬起一个 PendSV异常。
当CPU 退出SVC 后，它立即进入 PendSV，从而执行上下文切换。
当PendSV执行完毕后，将返回到任务 B，同时进入线程模式。
发生了一个中断，并且中断服务程序开始执行
在ISR 执行过程中，发生 SysTick 异常，并且抢占了该 ISR 。
OS执行必要的操作，然后悬起 PendSV异常以作好上下文切换的准备。
当SysTick 退出后，回到先前被抢占的 ISR 中，ISR 继续执行
ISR 执行完毕并退出后，PendSV服务例程开始执行，并且在里面执行上下文切换
当PendSV执行完毕后，回到任务 A，同时系统再次进入线程模式。

## Slide 39
9.2 NVIC 和中断控制
9.2.1 NVIC 概述
NVIC， 是Cortex-M3 处理器的一个重要组成部分。
NVIC 支持1 到240 外部中断输入和一个 不可屏蔽中断 (NMI) 输入。
NVIC 可以通过内存地址0xE000E000访问。
大多数中断控制/状态寄存器只能够在特权模式下访问。
Notes: 9.2 The NVIC and Interrupt Control
9.2.1 NVIC Overview
The Nested Vectored Interrupt Controller, or NVIC, is an integrated part of the Cortex-M3 processor.
The NVIC supports 1 to 240 external interrupt inputs and a Nonmaskable Interrupt (NMI) input.
The NVIC can be accessed as memory location 0xE000E000.
Most of the interrupt control/ status registers are accessible only in privileged mode.
39

## Slide 40
9.2.2 中断配置基础
每个外部中断有一些相应的寄存器，包括：
1.使能与除能寄存器
2.悬起与“解悬”寄存器
3.优先级寄存器
4.活动状态寄存器
一系列其它寄存器也可以影响中断进程
1. 异常屏蔽寄存器
2.向量表偏移量寄存器
3.软件触发中断寄存器
4.优先级分组位段
Notes: Each external interrupt has several registers associated with:
1. Enable and clear enable registers
2. Set-pending and clear-pending registers
3. Priority level
4. Active status
A number of other registers can also affect the interrupt processing:
1. Exception-masking registers
2. Vector Table Offset register
3. Software Trigger Interrupt register
4. Priority Group
40

## Slide 41
9.2.3 中断的使能与除能
中断使能寄存器通过两个地址来编程。
为了设置一个使能位，写向 SETENA 寄存器地址；
为了清除一个使能位， 写向CLRENA 寄存器地址。
外部中断： 上限到240；
所以有多个SETENA 和CLRENA 寄存器.
SETENA: 0xE000E100--0xE000E11C
CLRENA: 0xE000E180-0xE000E19C
Notes: The Interrupt Enable register is programmed via two addresses.
To set the enable bit, write 1 to the SETENA register address;
To clear the enable bit, write 1 to the CLRENA register address.
External interrupts: Up to 240;
So there are more than one SETENA and CLRENA register.
SETENA: 0xE000E100--0xE000E11C
CLRENA: 0xE000E180-0xE000E19C
41

## Slide 42
中断使能寄存器和中断清使能寄存器
名 | 类型 | 地址 | 复位值 | 描述
SETENA0 | R/W | 0xE000E100 | 0 | 0-31号外部中断使能
SETENA1 | R/W | 0xE000E104 | 0 | 32-63号外部中断使能
… | … | … | … | …
SETENA7 | R/W | 0xE000E11C | 0 | 224-239号外部中断使能
CLRENA0 | R/W | 0xE000E180 | 0 | 0-31 号外部中断清使能
CLRENA1 | R/W | 0xE000E184 | 0 | 32-63号外部中断清使能
… | … | … | … | 
CLRENA7 | R/W | 0xE000E19C | 0 | 224-239号外部中断清使能

## Slide 43
9.2.4 中断的悬起与解悬
如果一个中断发生，但是不能够立刻执行，它将被悬起。
中断悬起状态 可以通过中断设置悬起(SETPEND) 和中断解悬(CLRPEND) 寄存器来控制。
有多个SETPEND 和CLRPEND 寄存器。
SETPEND: 0xE000E200-0xE000E21C
CLRPEND: 0xE000E280-0xE000E29C
Notes: If an interrupt takes place but cannot be executed immediately, it will be pended.
The interrupt-pending status can be accessed through the Interrupt Set Pending (SETPEND) and Interrupt Clear Pending (CLRPEND) registers.
Similarly to the enable registers, there are more than one SETPEND and CLRPEND register.
SETPEND: 0xE000E200-0xE000E21C
CLRPEND: 0xE000E280-0xE000E29C
43

## Slide 44
Name | Type | Address | Reset Value | Description
SETPEND0 | R/W | 0xE000E200 | 0 | Pending for external interrupt #0-31
SETPEND1 | R/W | 0xE000E204 | 0 | Pending for external interrupt #32-63
… | … | … | … | …
SETPEND7 | R/W | 0xE000E21C | 0 | Pending for external interrupt #224-239
CLRPEND0 | R/W | 0xE000E280 | 0 | Clear pending for external interrupt #0-31
CLRPEND1 | R/W | 0xE000E284 | 0 | Clear pending for external interrupt #32-63
… | … | … | … | 
CLRPEND7 | R/W | 0xE000E29C | 0 | Clear pending for external interrupt #224-239
中断设置寄存器和中断清除寄存器
Notes: Interrupt Set Pending Registers and Interrupt Clear Pending Registers
44

## Slide 45
9.2.4.1 优先级
每一个外部中断都有一个相关联的优先级控制寄存器(3-8 bit位宽).
中断优先级控制寄存器(0xE000E400-0xE000E4EF)
Name | Type | Address | Reset Value | Description
PRI_0 | R/W | 0xE000E400 | 0 (8-bit) | Priority-level external interrupt #0
PRI_1 | R/W | 0xE000E401 | 0 (8-bit) | Priority-level external interrupt #1
… | … | … | … | ..
PRI_239 | R/W | 0xE000E4EF | 0 (8-bit) | Priority-level external interrupt #239
Notes: Priority
Each external interrupt has an associated priority-level register (a width of 3-8 bits).
Interrupt Priority-Level Registers(0xE000E400-0xE000E4EF
45

## Slide 46
9.2.4.2 活动状态
每一个外部中断都有一个开启状态位。当处理器开始执行中断处理程序时，该位设置为1；在中断返回时清零。
中断开启状态寄存器(0xE000E300-0xE000E31C)
Name | Type | Address | Reset Value | Description
ACTIVE0 | R | 0xE000E300 | 0 | Active status for external interrupt #0-31
ACTIVE1 | R | 0xE000E304 | 0 | Active status for external interrupt #32-63
… | … | … | … | …
ACTIVE7 | R | 0xE000E31C | 0 | Active status for external interrupt #224-239
Notes: Active Status
Each external interrupt has an active status bit. When the processor starts the interrupt handler, the bit is set to 1 and cleared when the interrupt return is executed.
Interrupt Active Status Registers
46

## Slide 47
9.2.4.3 PRIMASK 和 FAULTMASK 特殊功能寄存器
PRIMASK寄存器通过将当前的优先级改为0来除能所有异常。
该寄存器可以通过使用MRS和MSR命令来编程控制。
Example:
MOV R0, #1
MSR PRIMASK, R0 ; Write 1 to PRIMASK to disable all interrupts
MOV R0, #0
MSR PRIMASK, R0 ; Write 0 to PRIMASK to allow interrupts
FAULTMASK寄存器通过将当前的优先级改为-1来除能所有异常。
FAULTMASK 会在异常退出时自动清零。
Notes: PRIMASK and FAULTMASK Special Registers
The PRIMASK register disable all exceptions by changing the current priority level to 0.
It is programmable using MRS and MSR instructions.
Example:
MOV R0, #1
MSR PRIMASK, R0 ; Write 1 to PRIMASK to disable all interrupts
And:
MOV R0, #0
MSR PRIMASK, R0 ; Write 0 to PRIMASK to allow interrupts
The FAULTMASK register disable all exceptions by changing the current priority level to -1.
FAULTMASK is cleared automatically upon exiting the exception handler.
47

## Slide 48
9.2.4.4 BASEPRI特殊功能寄存器
BASEPRI 寄存器能够屏蔽优先级小于特定值的中断。
Example:
MOV R0, #0x60
MSR BASEPRI, R0 ; Disable interrupts with priority 0x60-0xFF
To cancel the masking:
MOV R0, #0x0
MSR BASEPRI, R0 ; Turn off BASEPRI masking
BASEPRI寄存器同样能够通过 BASEPRI_MAX 名称进行访问
Notes: The BASEPRI
The BASEPRI register disables interrupts with priority lower than a certain level.
Example:
MOV R0, #0x60
MSR BASEPRI, R0 ; Disable interrupts with priority 0x60-0xFF
To cancel the masking:
MOV R0, #0x0
MSR BASEPRI, R0 ; Turn off BASEPRI masking
The BASEPRI register can also be accessed using the BASEPRI_MAX register name.
Special Register
48

## Slide 49
使用BASEPRI_MAX 寄存器名访问时, 只能够改变到一个更高的优先级。
Example:
MOV R0, #0x60
MSR BASEPRI_MAX, R0 ; Disable interrupts with priority 0x60, ;0x61,..., etc
MOV R0, #0xF0
MSR BASEPRI_MAX, R0 ; This write will be ignored because
; it is lower level than 0x60
MOV R0, #0x40
MSR BASEPRI_MAX, R0 ; This write is allowed and change the ;masking level to 0x40
Notes: Using BASEPRI_MAX as a register, it can only be changed to a higher priority level.
49

## Slide 50
9.2.4.5 其它异常的配置寄存器
用法fault ，总线fault 以及存储器管理fault 都是特殊的异常，它们的使能控制是通过“系统Handler 控制及状态寄存器(SHCSR) ”（地址：0xE000_ED24）来实现的。各种faults的悬起状态和大多数系统异常的活动状态也都在该寄存器中。
Notes: Configuration Registers for Other Exceptions
Usage faults, memory management faults, and bus fault exceptions are enabled by the System Handler Control and State Register
The System Handler Control and State Register (0xE000ED24)
50

## Slide 51
系统Handler控制及状态寄存器SHCSR（地址：0xE000_ED24）
Bits | Name | Type | Reset Value | Description
18 | USGFAULTENA | R/W | 0 | Usage fault handler enable
17 | BUSFAULTENA | R/W | 0 | Bus fault handler enable
16 | MEMFAULTENA | R/W | 0 | Memory management fault enable
15 | SVCALLPENDED | R/W | 0 | SVC pended; SVCall was started but was replaced by a higher-priority exception
14 | BUSFAULTPENDED | R/W | 0 | Bus fault pended; bus fault handler was started but was replaced by a higher-priority exception
Notes: Configuration Registers for Other Exceptions
Usage faults, memory management faults, and bus fault exceptions are enabled by the System Handler Control and State Register
The System Handler Control and State Register (0xE000ED24)
51

## Slide 52
13 | MEMFAULTPENDED | R/W | 0 | Memory management fault pended; memory management fault started but was replaced by a higher-priority exception
12 | USGFAULTPENDED | R/W | 0 | Usage fault pended; usage fault started but was replaced by a higher-priority exception
11 | SYSTICKACT | R/W | 0 | Read as 1 if SYSTICK exception is active
10 | PENDSVACT | R/W | 0 | Read as 1 if PendSV exception is active
8 | MONITORACT | R/W | 0 | Read as 1 if debug monitor exception is active
7 | SVCALLACT | R/W | 0 | Read as 1 if SVCall exception is active
3 | USGFAULTACT | R/W | 0 | Read as 1 if usage fault exception is active
1 | BUSFAULTACT | R/W | 0 | Read as 1 if bus fault exception is active
0 | MEMFAULTACT | R/W | 0 | Read as 1 if memory management fault exception is active
(Continued)

## Slide 53
中断控制及状态寄存器ICSR（地址：0xE000_ED04）
Bits | Name | Type | Reset Value | Description
31 | NMIPENDSET | R/W | 0 | NMI pended
28 | PENDSVSET | R/W | 0 | Write 1 to pend system call; Read value indicates pending status
27 | PENDSVCLR | W | 0 | Write 1 to clear PendSV pending status
26 | PENDSTSET | R/W | 0 | Write 1 to pend SYSTICK exception; Read value indicates pending status
25 | PENDSTCLR | W | 0 | Write 1 to clear SYSTICK pending status
23 | ISRPREEMPT | R | 0 | Indicates that a pending interrupt is going to be active in the next step (for debug)
22 | ISRPENDING | R | 0 | External interrupt pending
21:12 | VECTPENDING | R | 0 | Pending ISR number
11 | RETTOBASE | R | 0 | Set to 1 when the processor is running an exception handler
9:0 | VECTACTIVE | R | 0 | Current running interrupt service routine
Notes: Interrupt Control and State Register (0xE000ED04)
53

## Slide 54
9.2.5 中断系统设置全过程的演示
当系统启动后，先设置优先级组寄存器。
如果需要重定位向量表，先把硬fault 和NMI 服务例程的入口地址写到新表项所在的地址中。
配置向量表偏移量寄存器，使之指向新的向量表
建立中断向量
为该中断设置优先级
使能该中断
Notes: 9.2.5 Example Procedures in Setting Up an Interrupt
1. Set up the priority group register.
2. Copy the hard fault and NMI handlers to a new vector table location.
3. Set up the Vector Table Offset register.
4. Read the Vector Table Offset register and calculate the correct memory location for the interrupt handler to Set up the interrupt vector.
5. Set up the priority level for the interrupt.
6. Enable the interrupt.
The program in assembly:
LDR R0, =0xE000ED0C ; Application Interrupt and Reset Control Register
LDR R1, =0x05FA0500 ; Priority Group 5 (2/6)
STR R1, [R0] ; Set Priority Group
54

## Slide 55
中断控制类型寄存器给出了所支持的输入中断的数量，粒度为32
中断控制类型寄存器(0xE000E004)
Bits | Name | Type | Reset Value | Description
4:0 | INTLINESNUM | R | – | Number of interrupt inputs in step of 32 0 = 1 to 32 1 = 33 to 64 …
Notes: Interrupt Controller Type Register gives the number of interrupt inputs supported, in granularities of 32.
Interrupt Controller Type Register (0xE000E004)
55

## Slide 56
9.2.6 软件中断
软件中断可由以下方式触发:
  1. SETPEND寄存器
  2. 软件触发中断寄存器(STIR)
软件触发中断寄存器STIR（地址：0xE000_ EF00）
系统异常(NMI, faults, PendSV等等)不能被该寄存器挂起
Bits | Name | Type | Reset Value | Description
8:0 | INTID | W | – | 影响编号为INTID 的外部中断，其悬起位被置位。例如，写入 8，则悬起IRQ #8
Notes: 9.2.6 Software Interrupts
Software interrupts can be generated by using:
1. The SETPEND register
2. The Software Trigger Interrupt Register (STIR)
Software Trigger Interrupt Register (0xE000EF00)
System exceptions (NMI, faults, PendSV, and so on) cannot be pended using this register.
56

## Slide 57
9.2.7 SysTick 定时器
系统定时器(SYSTICK)与NVIC集成在一起，能够用于产生一个SYSTICK 异常。
系统定时器由四个寄存器控制
SysTick控制及状态寄存器（地址：0xE000_ E010）
Bits | Name | Type | Reset Value | Description
16 | COUNTFLAG | R | 0 | 如果在上次读取本寄存器后，SysTick 已经计到了0，则该位为 1。如果读取该位，该位将自动清零
2 | CLKSOURCE | R/W | 0 | 0=外部时钟源(STCLK) 1=内核时钟(FCLK)
1 | TICKINT | R/W | 0 | 1=SysTick 倒数计数到0 时产生 SysTick 异常请求 0=数到0 时无动作
0 | ENABLE | R/W | 0 | SysTick 定时器使能位
Notes: 9.2.7 The SYSTICK Timer
The SYSTICK Timer is integrated with the NVIC and can be used to generate a SYSTICK exception.
The SYSTICK Timer is controlled by four registers.
Table 8.9 SYSTICK Control and Status Register (0xE000E010)
57

## Slide 58
SysTick重装载数值寄存器（地址：0xE000_ E014）
SysTick当前数值寄存器（地址：0xE000_ E018）
Bits | Name | Type | Reset Value | Description
23:0 | RELOAD | R/W | 0 | 倒数计数至零时，将被重装载的值
Bits | Name | Type | Reset Value | Description
23:0 | CURRENT | R/Wc | 0 | 读取时返回当前倒计数的值，写它则使之清零，同时还会清除在 SysTick 控制及状态寄存器中的 COUNTFLAG 标志
Notes: SYSTICK Reload Value Register (0xE000E014)
SYSTICK Current Value Register (0xE000E018)
58

## Slide 59
SysTick校准数值寄存器（地址：0xE000_ E01C）
Bits | Name | Type | Reset Value | Description
31 | NOREF | R | – | 1=没有外部参考时钟（STCLK 不可用） 0=外部参考时钟可用
30 | SKEW | R | – | 1=校准值不是准确的 10ms 0=校准值是准确的 10ms
23:0 | TENMS | R/W | 0 | 在10ms 的间隔中倒计数的格数。芯片设计者应该通过Cortex-M3的输入信号提供该数值。若该值读回零，则表示无法使用校准功能
Notes: SYSTICK Calibration Value Register
The SYSTICK Timer can also be used for:
1. as an alarm timer
2. for timing measurement
59

## Slide 60
- THE END -